RESULTS OF THE MGB GEOHAZARD ASSESSMENT

Province of Antique

I. ANINI-Y

The result of the MGB Rapid Field Assessment is as follows:

- There are six (6) barangays with high landslide susceptibility (Casay, Sagua,     Salvacion, San Ramon, Milagrosa and Igpalge).

- There are seven (7) barangays with moderate landslide susceptibility (Bayo, Pequeño, Nato, San Roque, Nasuli C, Igtumarom, Talisayan and Tagaytay).

- There are five (5) barangays with low landslide susceptibility (Butuan, Casay Viejo, Mabuyong, Lisub B, Bayo Grande).

- There are five (5) barangays with no landslide susceptibility (Iba, Magdalena,     Poblacion, San Francisco and Lisub A).

Table 1. Results of Landslide Assessment of the twenty-three (23) Barangays

| Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Casay | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Constant communication and updates with the Barangay Casay Viejo on geohazard situation. District 2 and Greenhills Subdivision are landslide-prone areas. |
| 2 | Sagua | High | Observe for presence of mass movements (e.g. landslides, tensions cracks). Develop an early warning device/system. |
| 3 | Salvacion | High | The barangay has high landslide susceptibility. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Landslide area in Sitio Tuhaw. |
| 4 | San Ramon | High | Monitor progress and observe for presence of mass movement (landslide, tension cracks). Observe for sunken or displaced roads surfaces. Constant communication and updates with barangays Tagaytay and Igtumaron on geohazard situation. San Ramon barangay road has high susceptibility to landslide. Activate BDCC. Area has a widespread creeping, tension cracks and slumping. Discuss the contingency planning for hazards of landslides in San Ramon. IEC on geohazards situation among residents. |
| 5 | Milagrosa | Moderate to High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/ system intended for landslide & flood hazards; Identify evacuation site; Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for sunken or displaced roads surfaces. Constant communication and updates with barangay Igpalge on geohazard situation. Activate BDCC |
| 6 | Igpalge | Moderate to High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device for landslide and flashflood. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for sunken or displaced road surfaces. Constant communication and updates with barangay Milagrosa on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 7 | Bayo Pequeño | Moderate | Observe for presence of mass movements (e.g. landslides, tension cracks). |
| 8 | Nato | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with barangay Salvacion on geohazard situation. Sitio Cansilayan is a landslide area. |
| 9 | San Roque | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 10 | Nasuli C | Low to Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning system for landslide and flashflood. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Constant Communication and updates with barangay Iba on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 11 | Igtumarom | Moderate - Brgy. Proper; High - in Puroks/Sitios in mountain area | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for sunken or displaced road surfaces. Inform residents of Igtumaron geohazard situation |
| 12 | Tagaytay | Moderate - Brgy. Proper; High - areas of Mt. Aliw-liw | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) especially on slopes of Mt. Aliw-liw. Develop an early warning device/system. Observe saturated ground or seeps in areas that are not typically wet. Observe sunken or displaced roads surfaces. Constant communication and updates with Brgys. San Ramon and Igtomarom. Widespread creeping and numerous tension cracks were observed in the area. Activate BDCC. |
| 13 | Talisayan | Moderate at the Barangay Proper and Purok 1 | Observe presence of mass movement (e.g. landslides, tension cracks). |
| 14 | Butuan | Low | Observe for presence of mass movements (e.g. landslides, tension cracks). |
| 15 | Casay Viejo | Low | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 16 | Mabuyong | Low | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Blue Ridge, Sitio Maricog, Sitio Bagacay and along the road to Brgy. Milagrosa are landslide prone areas. |
| 17 | Lisub B | Low at the barangay proper; Moderate at Purok 1 & 3 | Observe for presence of mass movements; (e.g. landslides, tension cracks). Develop an early warning device. |
| 18 | Bayo Grande | Low at the Barangay Proper; Moderate at Sitio Calamnugan | Observe for presence of mass movements; Activate Barangay Disaster Coordinating Council (BDCC). |
| 19 | Iba | None | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Punta Nasub, Sitio Rendon, Cresta de Gallo, Sitio Banderahan, Sitio Bulag are landslide prone areas. |
| 20 | Magdalena | None | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Sitio Pait, Sitio Igcaripa, Sitio Kababaan, Sitio Igbasya, Sitio Panabigan are landslide areas. |
| 21 | Poblacion | None | Observe for presence of mass movement (e.g. landslides, tension cracks) in Purok 8. |
| 22 | San Francisco | None | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 23 | Lisub A | None at the barangay proper; Low at Purok 2 and Purok 3 | Observe for presence of mass movements; (e.g. landslides, tension cracks). Develop an early warning device. Identify evacuation site. Activate Barangay Disaster Coordinating Council (BDCC). |

In terms of flood susceptibility, twelve (12) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the Twenty-Three (23) Barangays

| Barangay | Remarks/ Recommendations |
| --- | --- |
| 1 | Bayo Grande | Storm surge affects five households during typhoon season. River bank erosion along Sapa Malalim also affects Sitio Calamnugan. |
| 2 | Bayo Pequeño | Storm surge and coastal flooding during typhoon season also affects the area. |
| 3 | Butuan | Houses near the coast are affected by storm surge. |
| 4 | Casay | Moderate flash flood turbidity. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Sheet flooding depth of 10 ft. and coastal flooding during storm surge occurs. Constant communication and updates with Barangay Casay on geohazard situation. |
| 5 | Casay Viejo | Moderate flash flood turbidity. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 6 | Iba | Moderate flash flood turbidity. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop early warning system. Coastal flooding during storm surge. |
| 7 | Igpalge | High flash flood turbidity is common at Ibuc River. River bank erosion is common the area. |
| 8 | Igtumarom | Casay River inundation up to 5m high during heavy rainfall and extreme weather conditions. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Casay river. Observe for sunken or displaced road surfaces. |
| 9 | Lisub A | Identify evacuation site. Seven (7) households in Purok 1 and three (3) households in Purok 2 are affected by storm surge and coastal flooding (less than 0.5 m).River bank erosion along Talisay River also affects 5 houses. |
| 10 | Lisub B | Develop an early warning device. Purok 4 was affected by storm surge during the height of typhoon Frank. |
| 11 | Mabuyong | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Coastal flooding during storm surge occurs. Develop early warning system/device. |
| 12 | Magdalena | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 13 | Milagrosa | Flash flood with very high turbidity is common. |
| 14 | Nasuli C | River bank erosion is common in the area. |
| 15 | Nato | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity. Moderate flash flood turbidity. Coastal flooding occurs during storm surge. Develop early warning system/device. |
| 16 | Poblacion | Storm surge occurs along the municipal road. |
| 17 | Sagua | Storm surge affects one household. |
| 18 | Salvacion | Sheet flooding depth is high. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Coastal flooding occurs during storm surge. Develop early warning system/device. |
| 19 | San Francisco | Sheet flooding depth is high. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system. Coastal flooding occurs during storm surge. |
| 20 | San Ramon | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Hinarugan River. |
| 21 | San Roque | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system. Coastal flooding occurs during storm surge. |
| 22 | Tagaytay | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 23 | Talisayan | Moderate coastal flooding affects the barangay. |

II.  BARBAZA

The result of the field assessment is as follows:

- There are eleven (11) barangays with high landslide susceptibility (Bahuyan,  Binangbang Bario, Calapadan, Embrangga-an, Integasan, Lanas, Mablad,  Marirong, Tig-Alaran, Yapo and Cadiao)

- There are seven (7) barangays with moderate landslide susceptibility (Biga-a, Lombuyan, Mayos, Igtumarom, Soligao, Tabong-Tabong and Poblacion)

- There are three (3) barangays with low landslide susceptibility (Binanu-an, Baghari and Langcaon  (Evelio Javier)),

- There are thirteen (13) barangays with no landslide susceptibility.

Table 1. Results of landslide assessment of the thirty-four (34) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Bahuyan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. |
| 2 | Binangbang Bario | High | There are numerous tension cracks observed in the area. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood.Identify evacuation site. Identify relocation site for residents living at Brgy. Binangbang Bario. Discuss possibility of relocation with constituents and LGU. |
| 3 | Calapadan | High | Monitor progress and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide hazard.Identify evacuation site. Identify relocation site for residents living at Brgy. Calapadan. Activate BDCC and implement contingency planning for the barangay. |
| 4 | Embrangga-an | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living at the foot of the mountain and aalong the river. Constant communication and updates with the Poblacion on geohazard situation. Activate BDCC. Clear the river of landslide debris. |
| 5 | Integasan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Brgy. Marirong on geohazard situation. Activate BDCC. |
| 6 | Lanas | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood hazard. Identify relocation site for residents living at Brgy. Proper. The small community should be relocated to safer ground. Numerous active landslides and other mass wasting on steep slopes surrounding the area. |
| 7 | Mablad | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood.Identify new evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces.Identify relocation site for residents living at Purok 1,2, & 3. Constant communication & updates with Brgy. Cadiao on geohazard situation. Activate BDCC. |
| 8 | Marirong | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living at the foot of the mountains and those along riverbanks. Constant communication and updates with Brgy. Embranga-an on geohazard situation. Activate BDCC. |
| 9 | Tig-Alaran | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living along riverbank and foot of the mountains. Constant communication and updates with Brgy. Marirong on geohazard situation. Activate BDCC. |
| 10 | Yapo | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. |
| 11 | Cadiao | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood.Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces.Identify relocation site for residents living at Purok 1 & 2 (Barangay Cadiao). Constant communication and updates with Brgy. Maayos on geohazard situation. Activate BDCC. |
| 12 | Biga-a | Moderate to High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system for landslide. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces.Constant communication and updates with Brgy. Mablad & upper barangays like Cadiao & Maayos on geohazard situation. Relocate the houses of the Dimapilis Family that are adjacent to the hill and mountain slope. Activate BDCC. |
| 13 | Lombuyan | Moderate to High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood.Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces.Identify relocation site for residents living at Lombuyan. Constant communication and updates with Brgy. Biga-a on geohazard situation. Activate BDCC. |
| 14 | Mayos | Moderate to High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for the houses of Perfecto Family and residents living near the riverbank at Brgy. Mayos. Constant communication & updates with Brgy. Cadiao on geohazard situation.Activate BDCC. |
| 15 | Igtumarom | Moderate | Monitor progress of mass movement and observe for presence of mass movement (lanslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Constant communication and updates with Brgy. Soligao on geohazard situation. |
| 16 | Soligao | Moderate | Monitor progress of mass movement and observe for presence of mass movement (lanslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Constant communication and updates with Brgy. Esparagoza on geohazard situation. |
| 17 | Tabong-Tabong | Moderate | Monitor progress of mass movement and observe for presence of mass movement (lanslide, tension cracks). Develop an early warning device/system. Constant communication and updates with Brgy. Jinalinan on geohazard situation. |
| 18 | Poblacion | Moderate | Monitor progress and observe for presence of mass movement (landslide, tension cracks) |
| 19 | Binanu-an | Low (Brgy. Poper); High (Purok 5) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) for Purok 5 |
| 20 | Baghari | Low to Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for sunken or displaced roads surfaces. Avoid build-up on footslopes. |
| 21 | Langcaon (Evelio Javier) | Low | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Activate Barangay Disaster Coordinating Council (BDCC). |
| 22 | Magtulis | None (Brgy. Proper); High (Purok Dumangsal) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) for Purok Dumangsal |
| 23 | Beri | None |  |
| 24 | Binangbang Centro | None |  |
| 25 | Capoyuan | None |  |
| 26 | Cubay | None |  |
| 27 | Esparar | None |  |
| 28 | Gua | None |  |
| 29 | Igpalge | None |  |
| 30 | Ipil | None |  |
| 31 | Jinalinan | None |  |
| 32 | Lisub | None |  |
| 33 | Palma | None |  |
| 34 | San Antonio | None |  |
| 35 | Idao | Not accessed due to difficulty in accessing the area |  |
| 36 | Marigne | Not accessed due to difficulty in accessing the area |  |
| 37 | Mayabay | Not accessed due to difficulty in accessing the area |  |
| 38 | Nalusdan | Not accessed due to difficulty in accessing the area |  |
| 39 | San Ramon | Not accessed due to difficulty in accessing the area |  |

In terms of flood assessment, there are twenty-six (26) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the thirty-four (34) barangays

|  | Barangay | Remarks/Recommendation |
| --- | --- | --- |
| 1 | Baghari | Flash flood is very common along Binangbang River with high turbidity (debris and soil content). Develop an early warning device/system for flood hazard. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Avoid build-up along creek and set a buffer zone for land and residential development along Binangbang River |
| 2 | Bahuyan | None |
| 3 | Beri | Flooding caused by overflowing of Dalanas river during heavy rains. Sheet flooding with depth of greater than 1 m occurs seasonally. |
| 4 | Biga-a | Sheet flooding depth is 0.5-1 m. |
| 5 | Binangbang Bario | Flash flood with very high turbidity is very common in the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 6 | Binangbang Centro | Sheet flooding depth greater than 1 m. Flashflood common in the area. |
| 7 | Binanu-an | None |
| 8 | Cadiao | Flashflood with very high turbidity is very common in the area. |
| 9 | Calapadan | Flash flood with very high turbidity is very common along Igtiring Creek. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Igtiring creek. Avoid build-up along the creek. |
| 10 | Capoyuan | Sheet flooding depth is 0-0.5 m. |
| 11 | Cubay | Sheet flooding depth greater than 1 m. Flashflood commonly occurs along Binangbang River. River erosion also a problem. |
| 12 | Embrangga-an | Sheet flooding depth is greater than 1 m. Flashflood with high turbidity affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system. Identify evacuation site. |
| 13 | Esparar | None |
| 14 | Gua | Sheet flooding depth greater than 1 m. |
| 15 | Idao | Not accessed due to difficulty in accessing the area |
| 16 | Igpalge | Sheet flooding depth is 0.5-1 m. |
| 17 | Igtumarom | None |
| 18 | Integasan | Sheet flooding depth is greater than 1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 19 | Ipil | Flooding is caused by overflowing of Dalanas and Nalupa rivers. Storm surge also affects barangay. Sheet flooding depth greater than 1m. |
| 20 | Jinalinan | Sheet flooding depth greater than 1 m. |
| 21 | Lanas | The brgy. is along the flashflood path. Flash flood with very high turbidity is very common in Anahaw River. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Anahaw River. |
| 22 | Langcaon (Evelio Javier) | Inundation of Macalbag Creek affects the barangay road. |
| 23 | Lisub | None |
| 24 | Lombuyan | Flashflood with very high turbidity and riverbank erosion are very common in the area. Sheet flooding depth is 0.5-1 m. |
| 25 | Mablad | Flashflood with very high turbidity and riverbank erosion are very common in the area. Sheet flooding depth is 0.5-1 m. |
| 26 | Magtulis | None |
| 27 | Marigne | Not assessed due to difficulty in accessing the area |
| 28 | Mayabay | Not accessed due to difficulty in accessing the area |
| 29 | Mayos | Sheet flooding depth is 0.5-1 m. |
| 30 | Nalusdan | Not accessed due to difficulty in accessing the area |
| 31 | Marirong | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system. Identify evacuation site. Sheet flooding depth is greater than 1m. |
| 32 | Palma | Flashflood with moderate turbidity is common. Sheet flooding depth is greater than 1m. |
| 33 | Poblacion | None |
| 34 | San Antonio | Flooding caused by overflowing of Dalanas river during heavy rains. Sheet flooding with depth of greater than 1 m occurs seasonally. |
| 35 | San Ramon | Not accessed due to difficulty in accessing the area |
| 36 | Soligao | Flashflood with high turbidity affects the area. Bank scouring along Mamaraka River. |
| 37 | Tabong-Tabong | Rare occurrence of flooding with depth of less than 0.5m. |
| 38 | Tig-Alaran | Sheet flooding depth is greater than 1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Clear river and creeks of debris. |
| 39 | Yapo | None |

III. BELISON

The result of the MGB Rapid Field Assessment is as follows:

- There are no barangays with high landslide susceptibility.

- There is one (1) barangay with moderate landslide susceptibility (Buenavista).

- There is one (1) barangay with low landslide susceptibility (Mojon).

- There are nine (9) barangays with no landslide susceptibility.

Table 1. Results of Landslide Assessment of the Eleven (11) Barangays

| Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Buenavista | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 2 | Mojon | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 3 | Borocboroc | None |  |
| 4 | Concepcion | None |  |
| 5 | Delima | None |  |
| 6 | Ipil | None |  |
| 7 | Maradiona | None |  |
| 8 | Poblacion | None |  |
| 9 | Rombang | None |  |
| 10 | Salvacion | None |  |
| 11 | Sinaja | None |  |

In terms of flood susceptibility, seven (7) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the Eleven (11) Barangays

| Barangay | Remarks/ Recommendations |
| --- | --- |
| 1 | Borocboroc | During rainy season, flood depth reaches 0-0.5m caused and aggravated by the lack/absence of drainage. |
| 2 | Buenavista | None |
| 3 | Concepcion | There are 8 houses near Pasalcan Creek and about 50 houses along Sibalom River that were affected by stream inundation. Flood depth can reach up to more than 1m with duration of 1 day. Develop an early warning device/system for flood-related hazard. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living at Bacbac & Durog areas. Develop contingency planning for flood. Avoid build-up along riverbanks. |
| 4 | Delima | Sheet flood occurs in isolated small area along the coast |
| 5 | Ipil | None |
| 6 | Maradiona | Flood depth reaches 0-0.5m during continuous rainfall & because of clogged drainage. |
| 7 | Mojon | Flood depth reaches 0.5-1 m during rainy season on low areas. Flashflood regularity rare & flashflood turbidity low. Avoid build-up on banks of Pansalcan creek. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system for flood-related hazards. Riverbank scouring & rechanneling of Belison River can damage agricultural land. |
| 8 | Poblacion | Flashflood common and affects houses close to the riverbanks. Comprehensive drainage plan by LGUs is recommended |
| 9 | Rombang | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system for flood-related hazards. Activate BDCC and discuss contingency planning among constituents. More than 60% of Rombang's population affected by Typhoon Frank. High flood depth affects the entire barangay. |
| 10 | Salvacion | Flood depth reaches up to more than 0.5m. 90% of the population was affected by Typhoon Frank. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system for flood-related hazards. Observe the rechanneling of Sibalom River. Activate BDCC and discuss contingency planning among constituents. |
| 11 | Sinaja | Flash flood regularity is rare with moderate turbidity. Flood depth can reach up to more than 1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system for flood-related hazards. Identify evacuation site. Discuss contingency planning for flooding. Entire barangay was submerged to flood waters during typhoons Frank (2008), Undang (1980s), Mameng (1980s) among others. The school site was also affected with flood. Sinaja is one of the hard hit areas in Belison During Typhoon Frank. |

IV.  BUGASONG

The result of the MGB Rapid Field Assessment is as follows:

- There are six (6) barangays with high landslide susceptibility (Anilawan, Arangote, Sabang East, Yapu, Zaragosa, Pangalcagan).

- There are two (2) barangays with moderate landslide susceptibility (Maray, Bagtason)

- There are three (3) barangays with low landslide susceptibility (Tagudtud South, Lacayon, Tono-an)

- There are fifteen (15) barangays with no landslide susceptibility.

- Barangay Igsoro was not assessed due to poor weather condition and difficulty of access during the time of the survey.

Table 1. Results of Landslide Assessment of the twenty-six (26) Barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Anilawan | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 2 | Arangote | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for saturated ground or seeps in areas that are not typically wet, sunken or displaced road surfaces. Activate Barangay Disaster Coordinating Council (BDCC). Old and active landslide are located in Sitio Laguna and Tanayan. Farmlands are affected by these landslides. |
| 3 | Sabang East | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. School is highly susceptible to landslides.Identify alternative site for the school. |
| 4 | Yapu | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site for barangay proper and school. |
| 5 | Zaragoza | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Observe for saturated group or seeps in areas that are not typically wet. |
| 6 | Pangalcagan | Moderate to high | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 7 | Maray | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 8 | Bagtason | Low to moderate | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Identify relocation site for residents living at Sitio Seo. |
| 9 | Tagudtud South | Low | Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). |
| 10 | Lacayon | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 11 | Tono-an | Low (Brgy. Proper); Moderate (along roadcuts) | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 12 | Camangahan | None |  |
| 13 | Centro Ilawod (Pob.) | None |  |
| 14 | Centro Ilaya (Pob.) | None |  |
| 15 | Centro Pojo (Pob.) | None |  |
| 16 | Cubay North | None |  |
| 17 | Cubay South | None |  |
| 18 | Guija | None |  |
| 19 | Igbalangao | None |  |
| 20 | Ilaures | None |  |
| 21 | Jinalinan | None |  |
| 22 | Paliwan | None |  |
| 23 | Sabang West | None |  |
| 24 | Tagudtud North | None |  |
| 25 | Talisay | None |  |
| 26 | Tica | None |  |
| 27 | Igsoro | Not assessed due to difficulty in accessing the area |

In terms of flood susceptibility, twenty-six (26) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the twenty-six (26) Barangays

|  | Barangay | Remarks/Recommendations |
| --- | --- | --- |
| 1 | Anilawan | None |
| 2 | Arangote | Some portions of the road going towards the barangay proper are transected by creeks, which could cause localized flooding in these areas. |
| 3 | Bagtason | Seasonally flooded with depth greater than 1 meter. |
| 4 | Camangahan | Sitio Inulingan experiences coastal flooding. |
| 5 | Centro Ilawod (Pob.) | Develop an early warning device/system. Low-lying portions in Sitio Barcelo affect ricefields. Erosion along Sabang River is noted. |
| 6 | Centro Ilaya (Pob.) | Develop an early warning device/system. Erosion along Sabay river. Flooding is confined to Sabang East River affecting ricefields.The barangay is seasonally flooded. |
| 7 | Centro Pojo (Pob.) | Develop an early warning device/system. Low-lying areas in Sitio Atay-atay have high flood susceptibility affecting ricefields and 70 households. The barangay is seasonally flooded. Flooding due to improper drainage. |
| 8 | Cubay North | Susceptible to sheet floodign possibly from overflow of water from shallow river bed. Seasonally flooded with depth of 0-0.5 meter. |
| 9 | Cubay South | Susceptible to sheet floodign possibly from overflow of water from shallow river bed. Seasonally flooded with depth of 0.5-1 meter. |
| 10 | Guija | Develop an early warning device/system. Storm surge and coastal flooding affects 109 households in the barangay. Seasonally flooded with depth of 0-0.5 meter. |
| 11 | Igbalangao | None |
| 12 | Ilaures | Flash flood with very high turbidity is very common. Seasonally flooded with depth of 0.5-1 meter. |
| 13 | Igsoro | Not assessed due to difficulty in accessing the area |
| 14 | Jinalinan | Purok 1 has low flood susceptibility affecting 50 households. Storm surge affects Puroks 1 and 2. Riverbank erosion along Lumanggab River. Seasonally flooded with depth of 0-0.5 meter. |
| 15 | Lacayon | Sheet flooding confined to low lying areas close to the river. Seasonally flooded with depth of 0-0.5 meter. |
| 16 | Maray | None |
| 17 | Paliwan | Flash flood with moderate turbidity is very common. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Develop an early warning device/system. Constant communication and updates with the Barangay Cubay on geohazard situation. |
| 18 | Pangalcagan | Seasonally flooded with depth more than 1 meter. |
| 19 | Sabang East | None |
| 20 | Sabang West | Identify safe evacuation site. Riverbank erosion along Sabay river. Seasonally flooded with depth of 0-0.5 meter in the barangay proper and Puroks 1, 3 and 4. |
| 21 | Tagudtud North | Seasonally flooded with depth of 0.5-1 meter. |
| 22 | Tagudtud South | None |
| 23 | Talisay | Seasonally flooded with depth of 0.5-1 meter. |
| 24 | Tica | Seasonally flooded with depth of 0.5-1 meter. |
| 25 | Tono-an | Overflowing of Tono-an creek is the source of flood water. Seasonally flooded with depth of 0-0.5 meter. |
| 26 | Yapu | None |
| 27 | Zaragoza | None |

V. CULASI

The result of the field assessment is as follows:

- There are six (6) barangays with high landslide susceptibility (Alojipan, Batonan , Norte, Batonan Sur, Salde, San Luis and Valderrama)

- There are eight (8) barangays with moderate landslide susceptibility (Paningayan, Flores, Carit-an, Magsaysay (Balua), Osorio, San Pascual, San Vicente and Simbola)

- There are four (4) barangays with low landslide susceptibility (Malalison Island,     San Gregorio, Tigbobolo and Tinabusan)

- There are twenty-six (26) barangay propers with no landslide susceptibility

Table 1. Results of landslide assessment of the forty-four (44) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Alojipan | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Camancijan on geohazard situation. Activate BDCC. Previous barangay proper is further up but was vacated due to landslides. |
| 2 | Batonan Norte | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Batonan Sur on geohazard situation. |
| 3 | Batonan Sur | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Brgy. Batonan Norte on geohazard situation. |
| 4 | Salde | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. |
| 5 | San Luis | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Condes on geohazard situation. Activate BDCC. Warn people living/working along the slopes. Landslide areas are Sitio Bacolod, Sitio Kilat, Sitio Sooc. |
| 6 | Valderrama | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living along the river. Constant communication and updates with the Barangay San Gregorio on geohazard situation. Activate BDCC. . |
| 7 | Paningayan | Moderate (Brgy. Proper); High (Sitio Patag) | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) |
| 8 | Flores | Moderate to High the area is also susceptible to rockfall and rockslides. | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flashflood hazards. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Brgy. Flores especially houses adjacent to the mountain slopes and near the Tibiao River. Constant communication and updates with Brgy. San Vicente on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC) |
| 9 | Carit-an | Moderate | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Balac-Balac Sur on geohazard situation. |
| 10 | Magsaysay (Balua) | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) |
| 11 | Osorio | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) |
| 12 | San Pascual | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Inform the residents about the landslide threats |
| 13 | San Vicente | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flashflood hazards. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. San Luis on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC) |
| 14 | Simbola | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) |
| 15 | Malalison Island | Low in the Barangay proper; but moderate to high susceptibility to landslides in areas with steep slopes. | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) Particularly in areas with relatively steep slopes. |
| 16 | San Gregorio | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 17 | Tigbobolo | Low | Observe for presence of mass movement (landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Constant communication and updates with Brgy. Batonan Sur on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 18 | Tinabusan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 19 | Bagacay | None - Barangay Proper; Moderate to high for the mountain bounding the eastern of the barangay proper | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) for the mountains bounding the barangay. Identify evacuation site. |
| 20 | Batbatan Island | None (Brgy. Proper); Moderate (Sitio Camanga); high susceptibility to landslide in Sitio Recodo. | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 21 | Bitadton Sur | None in Barangay Proper; High for mountain bounding the eastern side of the barangay | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Avoid settlement at the foot of the mountain bounding the eastern side of the barangay. The barangay is also prone to storm surge, tsunami and liquefaction. |
| 22 | Bitadton Norte | None in Barangay Proper; High for mountain bounding the eastern side of the barangay proper | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. |
| 23 | Camancijan | None in Barangay Proper; High in Purok 1 | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) in Purok 1. Landslide due to 1990 earthquake in Purok 1 is noted. A landslide also occurred in Purok 1 during the height of typhoon Frank. Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Constant communication and updates with Brgy. Valderama. Activate BDCC. |
| 24 | Buenavista | None in barangay proper; Low in Sitio San Gabriel | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 25 | Naba | None in Barangay Proper; Moderate for the mountain bounding the southern and eastern portion of the barangay | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Identify relocation site for residents living adjacent to Naba River. Avoid settlement at the foot of the hill/mountain bounding the barangay and adjacent to Naba River. |
| 26 | Balac-balac | None |  |
| 27 | Bita | None |  |
| 28 | Buhi | None |  |
| 29 | Caridad | None |  |
| 30 | Centro Norte (Pob.) | None |  |
| 31 | Centro Sur (Pob.) | None |  |
| 32 | Condes | None |  |
| 33 | Esperanza | None |  |
| 34 | Fe | None |  |
| 35 | Jalandoni | None |  |
| 36 | Janlagasi | None |  |
| 37 | Lamputong | None |  |
| 38 | Lipata | None |  |
| 39 | Malacañang | None |  |
| 40 | Maniguin Island | None |  |
| 41 | Poblacion | None |  |
| 42 | San Antonio | None |  |
| 43 | San Juan | None |  |
| 44 | Tomao | None |  |

In terms of flood assessment, there are thirty-six (36) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the forty-four (44) barangays

|  | Barangay | Remarks/Recommendation |
| --- | --- | --- |
| 1 | Alojipan | Seasonal sheet flooding with depth of greater than 1m occurs. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Coordinate with municipality on how to clear river channel of landslide debris. Develop an early warning device/system. Identify relocation site for houses along the river, near landslide areas. |
| 2 | Bagacay | Avoid building houses adjacent to Panganta River. Bank erosion a problem. Seasonal sheet flooding with depth of 0.5-1m occurs. |
| 3 | Balac-balac | Flashflood with moderate turbidity affects the area. Rare sheet flooding with depth of less than 0.5m. |
| 4 | Batbatan Island | None |
| 5 | Batonan Norte | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 6 | Batonan Sur | Rare sheet flooding with depth of greater than 1m. |
| 7 | Bita | None |
| 8 | Bitadton Norte | Flashflood with high turbidity affects the area. The barangay is also prone to liquefaction and tsunami. Seasonal sheet flooding with depth of greater than 1m. |
| 9 | Bitadton Sur | Seasonal sheet flooding with depth of greater than 1m occurs. |
| 10 | Buenavista | Seasonal sheet flooding with depth of less than 0.5m. |
| 11 | Buhi | Sheet flooding with depth of 0.5-1m occurs seasonally. |
| 12 | Camancijan | The barangay will possibly be affected by flashflood due to landslide damming upstream. Detailed investigation is recommended. Overflowing of Bacong River is the main reason why flooding occurs in the barangay. Purok 1 lies on a former river channel and is therefore moderately susceptible to flood with depth of 0.5 to 1 meter, which affects about 100 households. Puroks 2, 5 and 6 have low flood susceptibility. Purok 3 has moderate susceptiblity to flood. The river protection (dike) along Bacong River was washed out during the height of typhoon Frank. Dredging of shallow riverbed is recommended. Identify relocation site for residents living adjacent to Bacong River. |
| 13 | Caridad | Sheet flooding with depth of greater than 1m occurs in Purok 1&3 due to overflowing of Panganta Creek. High in Purok 1 & 3 (overflowing of Panganta Creek) |
| 14 | Carit-an | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Rare occurrence of sheet flooding with depth of less than 1m. |
| 15 | Centro Norte (Pob.) | The barangay will possibly be affected by flashflood due to landslide damming upstream. Detailed investigation is recommended. Develop an early warning device/system flood and flashflood hazards. The barangay lies on a former river channel. Flooding in the barangay is mainly due to overflowing of Badiawis Creek and Bacong River. Puroks 1, 4, 5, 6 and 7 have low flood susceptibility. Purok 2 has high flood susceptibility affecting 20 households. Sheet flooding depth reaches greater than 0.5m. |
| 16 | Centro Sur (Pob.) | The barangay will possibly be affected by flashflood due to landslide damming upstream. Detailed investigation is recommended. Puroks 2 and 3 have low flood susceptibility while Puroks 4, 5 and 6 have high flood susceptibility with depth of greater than 1 meter. Flooding in the barangay is mainly due to overflowing of Badiawis Creek and Bacong River. Riverbank erosion and storm surge also affect the area. |
| 17 | Condes | None |
| 18 | Esperanza | Develop an early warning device/system. Identify relocation site for residents living adjacent to Panganta River. Avoid settlement adjacent to the Panganta River. Coastal area is prone to liquefaction, tsunami and storm surge. Dredging of and implementing engineering measures (e.g., dike) along the Panganta River are recommended. This drainage has reached a critical level (i.e just a few meters below the barangay area). Sheet flooding with depth of greater than 1m is seasonal. |
| 19 | Fe | Seasonal sheet flooding with depth of greater than 1m. |
| 20 | Flores | Flashflood with very high turbidity affects the area. |
| 21 | Jalandoni | Develop an early warning device/system. Identify evacuation site. The barangay will possibly be affected by flashflood due to landslide damming upstream. Detailed investigation is recommended. Puroks 1, 4 and 5 have low flood susceptibility. Puroks 2 and 3 have moderate flood susceptibility. Purok 7 has high flood susceptibility affecting 30 households. Riverbank erosion along Bacong River is also noted. |
| 22 | Janlagasi | Sheet flood confined in low lying rice fileds |
| 23 | Lamputong | Storm surge affects the area. Seasonal sheet flooding with depth of less than 0.5m. |
| 24 | Lipata | Sitio Tapican is affected by storm surge. Seasonal sheet flooding with depth of less than 0.5m. |
| 25 | Magsaysay (Balua) | None |
| 26 | Malacañang | Flashflood with high turbidity affects the area. Rare sheet flooding with depth greater than 1m. |
| 27 | Malalison Island | None |
| 28 | Maniguin Island | Coastal area prone to storm surge and flooding. Rare sheet flooding with depth of less than 0.5m. |
| 29 | Naba | Areas along the coast are prone to storm surge and liquefaction. Seasonal sheet flooding with depth less than 0.5m. |
| 30 | Osorio | None |
| 31 | Paningayan | Flooding due to overflowing of Paningayan River. Seasonal sheet flooding with depth greater than 1m. |
| 32 | Poblacion | The barangay will possibly be affected by flashflood due to landslide damming upstream. Detailed investigation is recommended. Develop an early warning device/system. Erosion along Badiawis Creek and Bacong River affects the area. The barangay lies on a former swamp. Puroks 1 and 5 are affected by storm surge. Puroks 2, 4 and 7 are highly susceptible to flood. Purok 3 is moderately susceptible to flood while Purok 6 is affected by coastal flooding and storm surge. Sheet flooding with depth greater than 1m is seasonal. |
| 33 | Salde | None |
| 34 | San Antonio | Flashflood with moderate turbidity affects the area. Rare sheet flooding with depth of less than 0.5m. |
| 35 | San Gregorio | None |
| 36 | San Juan | Sheet flooding with depth greater than 1m occurs in Purok 4. |
| 37 | San Luis | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Flashflood with moderate turbidity affects the area. Seasonal sheet flooding with depth greater than 1m occurs seasonally. |
| 38 | San Pascual | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Rare flash flooding with moderate turbidity (debris and soil content). |
| 39 | San Vicente | Riverbank erosion is also seen in the area. |
| 40 | Simbola | Flashflood commonly affects the area. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 41 | Tigbobolo | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Seasonal sheet flooding with depth less than 0.5m affects the barangay. |
| 42 | Tinabusan | None |
| 43 | Tomao | The barangay will possibly be affected by flashflood due to landslide damming upstream. Flooding in the area is mainly due to overflowing of Baywan Creek and Bacong River. Puroks 2 and 3 are moderately susceptible to flood, affecting more than 50 households and agricultural areas. |
| 44 | Valderrama | Seasonal sheet flooding with depth greater than 1m occurs seasonally. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Coordinate with municipality on how to clear river channel of landslide debris. Develop an early warning device/system. Identify relocation site for residents of the barangay since it is located at the mouth of the river and thus always in danger from flashfloods. Constant communication and updates with the Barangay San Gregorio on geohazard situation. Activate BDCC. Constant communication with Brgy. Alojipan for updates on water level upstream and possible damming. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

VI.  HAMTIC

The result of the field assessment is as follows:

- There are seventeen (17) barangays with high landslide susceptibility (Asluman, Banawon, Bongbongan I, Bongbongan II, Botbot, Calacja II, Cantulan, Caromangay, Gen. Fullon, Igbical, Igbucagay, Mapatag, Masanag, Nalihawan, Pamandayan, Paso-Jungao and Pili II)

- There are seven (7) barangays with moderate landslide susceptibility (Bongbongan III, Pili I, Apdo, Calacja  I, Casalngan, Del Pilar and Suloc)

- There are two (2) barangays with low landslide susceptibility (Fabrica and Linaban)

- There are twenty-three (23) barangays with no landslide susceptibility

Table 1. Results of landslide assessment of the forty-nine (49) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Asluman | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Mapatag on geohazard situation. Landslide occurrence at Sitio Hacienda. |
| 2 | Banawon | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Mapatag on geohazard situation. Soil creep observed at Severo Osunero Elementary School and one house is located at the top of the creep. |
| 3 | Bongbongan I | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Igbical on geohazard situation. Landslide area is at Sitio Gintabawan. |
| 4 | Bongbongan II | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Igbical on geohazard situation. Landslide at barangay proper affected three houses. |
| 5 | Botbot | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 6 | Calacja II | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living at Sitio Patlao and Sitio Simbulawan. |
| 7 | Cantulan | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system for landslides. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 8 | Caromangay | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 9 | Gen. Fullon | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces.Constant communication and updates with Barangay Banawon on geohazard situation. Two houses were buried by a landslide (1985). |
| 10 | Igbical | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/ system. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Ingwan on geohazard situation. Landslide area is at Sitio Paho. |
| 11 | Igbucagay | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Barangay hall rests on an unstable ground. Look for a possible relocation site. Implement slope stabilization measures. |
| 12 | Mapatag | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Asluman on geohazard situation. Landslide occurrence at Igay. |
| 13 | Masanag | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Bongbongan 1 & 2 on geohazard situation. Landslide in Sitio Ayutay affected 17 households and landslide in Sitio Plotchina affected 35 households. Relocate houses affected by landslides and those along the river. |
| 14 | Nalihawan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Bongbongan 1 & 2 on geohazard situation. Landslide area is at Sitio Igwakat, Igtamokol, Malibud. |
| 15 | Pamandayan | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system for landslide-related hazard. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Activate Barangay Disaster Coordinating Council (BDCC). |
| 16 | Paso-Jungao | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for for residents living at Paso-jungao. Activate Barangay Disaster Coordinating Council (BDCC). |
| 17 | Pili II | High | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system for Landslide and Flashflood. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Constant communication and updates with Barangay Pili I on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 18 | Bongbongan III | Moderate to High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Relocate Bongbongan III Elementary School. Constant communication and updates with Barangay Pamandayan on geohazard situation. |
| 19 | Pili I | Moderate to High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system for landslide and flood hazards. Observe for saturated ground or seeps in areas that are not typically wet. Activate Barangay Disaster Coordinating Council (BDCC). |
| 20 | Apdo | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Identify relocation site for residents living at Purok 3. |
| 21 | Calacja I | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Identifyevacuation site. |
| 22 | Casalngan | Moderate | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 23 | Del Pilar | Moderate | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). |
| 24 | Suloc | Moderate | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Avoid settlement at the top and at the foot of the slope. |
| 25 | Fabrica | Low in barangay proper; high in Purok 1 and near Gen. Leandro Fullon National School. | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Inform residents of Purok 1 regarding the danger posed by the presence of landslide in their area. Look for relocation site for Purok 1. Implement slope stabilization measures. There is an urgency to find a new location for the school since it is situated on a very unstable ground and rockfall occurrences have been reported in slopes adjacent to it. |
| 26 | Linaban | Low | Observe presence of mass movement (e.g. landslides, tension cracks). |
| 27 | Guintas | None – Brgy. Proper; High – Sitio Puro | Monitor progress of mass movement. Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/ system. |
| 28 | Ingwan-Batangan | None at the barangay proper; High at portions of Purok 2 (Mt. Turo-Turo ni Indo); High at Purok 3, Tacas Campsite | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) in Purok 2. Observe presence of mass movement (e.g. landslides, tension cracks) in Puroks 2, 3, Tacas and Campsite. Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Small landslide during the height of typhoon Frank. |
| 29 | Poblacion V | None at the barangay proper; Purok Tabangan - moderate; Camarin – low | Observe presence of mass movement (e.g. landslides, tension cracks) at Sitios Tabangan and Camarin. Develop an early warning device/ system. |
| 30 | Bia-anan | None |  |
| 31 | Bodbudan | None |  |
| 32 | Buhang | None |  |
| 33 | Calala | None |  |
| 34 | Caridad | None |  |
| 35 | Dangcalan | None |  |
| 36 | Funda | None |  |
| 37 | Inabasan | None |  |
| 38 | La Paz | None |  |
| 39 | Evelio B. Javier (Lanag) | None |  |
| 40 | Mahandog | None |  |
| 41 | Piape I | None |  |
| 42 | Piape II | None |  |
| 43 | Piape III | None |  |
| 44 | Poblacion I | None |  |
| 45 | Poblacion II | None |  |
| 46 | Poblacion III | None |  |
| 47 | Poblacion IV | None |  |
| 48 | Pu-Ao | None |  |
| 49 | Villavert- Jimenez | None |  |

In terms of flood assessment, there are thirty-eight (38) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the forty-nine (49) barangays

|  | Barangay | Remarks/Recommendation |
| --- | --- | --- |
| 1 | Apdo | None |
| 2 | Asluman | Coastal Flooding exacerbated by high tide. Bank erosion along Asluman river affects barangay Asluman. Seasonal sheet flooding with depth of 0.5-1m. Develop an early warning device/ system. |
| 3 | Banawon | Water is only confined at the channel. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 4 | Bia-anan | Sheet flooding depth is greater than 1m. River channel is silted. |
| 5 | Bongbongan I | Flashflood with moderate turbidity is very common. Sheet flooding depth is greater than 1m. Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 6 | Bongbongan II | Flashflood with moderate turbidity is very common. Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Seasonal sheet flooding with depth of more than 1m. |
| 7 | Bongbongan III | Flashflood with moderate turbidity commonly affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Erosion along Bongbongan River affects plantations and ricefields. Seasonal sheet flooding with depth of 0.5-1m. |
| 8 | Botbot | None |
| 9 | Bodbudan | Low flash flood turbidity is rare. Seasonal sheet flooding with depth of 0.5-1m. |
| 10 | Buhang | River bank erosion |
| 11 | Calacja I | None |
| 12 | Calacja II | River is eroding parts of Calacja. |
| 13 | Calala | Sheet flooding depth is greater than 1m in Sitio Puro. Flooding in barangay proper is less than 0.5m. River channel is silted. |
| 14 | Cantulan | Very high flash flood turbidity is very common. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 15 | Caridad | Forty four houses were destroyed by floods during typhoon Frank. Seasonal sheet flooding with depth of greater than 1m. |
| 16 | Caromangay | None |
| 17 | Casalngan | None |
| 18 | Dangcalan | Seasonal sheet flooding with depth of 0.5-1m. |
| 19 | Del Pilar | None |
| 20 | Fabrica | None |
| 21 | Funda | Sitio Binggay is affected by river bank erosion. Seasonal sheet flooding with depth of greater than 1m. |
| 22 | Gen. Fullon | Moderate flashflood turbidity occurs, but rare. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Bank erosion along Tina River. Rare sheet flooding with depth of greater than 1m. |
| 23 | Guintas | Seasonal sheet flooding with depth of 0.5-1m. |
| 24 | Igbical | Flashflood with moderate turbidity is very common. Flood depth more than 1 m. Develop an early warning device/ system. Identify evacuation site. Identify relocation site for houses along the river. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 25 | Igbucagay | None |
| 26 | Inabasan | Seasonal sheet flooding with depth of 0.5-1m. |
| 27 | Ingwan-Batangan | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Thirteen (13) households along Hamtic River and Ingwan Creek are affected by erosion and flood during typhoon season. Hamtic river channel shifts yearly. Seasonal sheet flooding with depth of 0.5-1m. |
| 28 | La Paz | Storm surge affects 13 households in the barangay. Develop an early warning device/ system. Identify evacuation site. |
| 29 | Evelio B. Javier (Lanag) | Seasonal sheet flooding with depth of 0.5-1m. |
| 30 | Linaban | None |
| 31 | Mahandog | Mahandog river overflow is causing the flooding in the area. Sheet flooding depth is greater than 1m. |
| 32 | Mapatag | Moderate flash flood turbidity is very common. Sheet flooding depth is greater than 1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 33 | Masanag | Flood depth more than 1 m. Flashflood very common. Develop an early warning device/ system. Identify evacuation site. Identify relocation site for houses along the river. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 34 | Nalihawan | Flood depth more than 1 m. Flashflood very common. Develop an early warning device/ system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 35 | Pamandayan | Flashflood with moderate turbidity affects the area. Seasonal sheet flooding with depth of 0.5-1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Pamandayan River. |
| 36 | Paso-Jungao | Flash flood is common. |
| 37 | Piape I | Flooding due to constricted creeks. Sheet flooding depth is greater than 1m. |
| 38 | Piape II | Seasonal sheet flooding with depth less than 0.5m. |
| 39 | Piape III | Seasonal sheet flooding with depth of 0.5-1m. |
| 40 | Pili I | Flashflood with moderate turbidity affects the area. Seasonal sheet flooding with depth of 0.5-1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 41 | Pili II | Flash flood with very high turbidity is very common. |
| 42 | Poblacion I | Seasonal sheet flooding with depth of less than 0.5m. Develop an early warning device/ system. Identify evacuation site. Seventy-two (72) households situated in the coastal areas are affected by coastal flooding and storm surge. |
| 43 | Poblacion II | Develop an early warning device/ system. Constant communication and updates with Barangays Poblacion 5,4 &3. Six households located along Hamtic River are affected by flooding. Sheet flooding depth less than 0.5m. |
| 44 | Poblacion III | Develop an early warning device/ system. Constant communication and updates with Barangay Pasungao on flood hazard situation. Zone 7 has high susceptibility to flood, affecting thirty (30) houses. Flooding also occurs at the boundary of barangay Poblacion 3 & 4. |
| 45 | Poblacion IV | Riverbank erosion along Hamtic River. Sheet flooding depth is greater than 1m in low-lying portions of the barangay. Develop an early warning device/ system. Identify evacuation site. |
| 46 | Poblacion V | Numerous houses located along Hamtic River have low flood susceptibility (Purok Dike). Riverbank erosion along Hamtic River is also noted. Constant communication and updates with Brgy. Ingwan Batangan on flood hazard situation. Sheet flooding depth is less than 0.5m. |
| 47 | Pu-Ao | Seasonal sheet flooding with depth greater than 1m. |
| 48 | Suloc | None |
| 49 | Villavert- Jimenez | None |

VII. LAUA-AN

The result of the MGB Rapid Field Assessment is as follows:

- There are nineteen (19) barangays with high landslide susceptibility (Banban, Liberato, Necesito, Pandanan, Virginia, Bongbongan, Canituan, Bo. Laua-an, Cabariwan, Poblacion, Capnayan, Leon, Santiago, Latasan, Tibacan, Mauno Maybunga, Pascuala and Paningayan).

- There are eight (8) barangays with moderate landslide susceptibility (Oloc, Lupa-an, Omlot, Jinalinan, Intao, Jaguiquican, Tigunhao and Maria).

- There are six (6) barangays with low landslide susceptibility (Guimbanga-an, Lactudan, Casit-an, Igtadiao, Bagongbayan and Lugta).

- There are four (4) barangays with no landslide susceptibility (Liya-Liya, Guisijan, Lindero and Cadajug).

- There are three (3) barangays that were not assessed due to difficulty in accessing the area (Guiamon, Magyapo and San Ramon).

Table 1. Results of Landslide Assessment of the Thirty-Seven (37) Barangays

| Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Banban | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system on landslide hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Mauno on geohazard situation. Occurrence of landslide at the mountain just above the barangay proper during Typhoon Frank. The slope of the mountain is almost vertical and the rock types composed of conglomerate and interbedded sandstone, siltstone and mudstone. |
| 2 | Bongbongan | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Constant communication and updates with Brgy. Lupa-an on geohazard situation. |
| 3 | Cabariwan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system on landslide hazard. Identify an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Poblacion on geohazard situation. Occurrence of landslide in Bariri Mountain. |
| 4 | Canituan | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Laua-an on geohazard situation. |
| 5 | Capnayan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for sunken or displaced road surfaces. Constant communication and updates with MDCC on geohazard situation. |
| 6 | Latasan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Constant communication and updates with Brgy. Tigunhao on geohazard situation. Activate BDCC. |
| 7 | Laua-an | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Constant communication and updates with Brgy. Canituan on geohazard situation. |
| 8 | Leon | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system on landslide hazard. Identify evacuation site. Constant communication and updates with the Barangay Paningayan & Santiago on geohazard situation. Contingency planning on landslide and flashflood hazards. |
| 9 | Liberato | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Relocation of 2 households located approximately 5 meters away from landslide area. |
| 10 | Necesito | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. |
| 11 | Pandanan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Slopes bounding the barangay highly unstable. School behind an unstable slope is situated 15 m SE of an active landslide. Avoid settlement at the foot of the slope and adjacent to the Paningayan River. |
| 12 | Poblacion | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Intao on geohazard situation. Landslide at Estaca Mountain part of the barangay. |
| 13 | Santiago | High | Inform residents of the high susceptibility of the area to landslide. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide hazard. Identify evacuation site. Numerous recent/active landslides were noted on slopes surrounding the brgy. |
| 14 | Tibacan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Brgy. Tibakan. Constant communication and updates with Brgy. Santiago on geohazard situation. Activate BDCC. |
| 15 | Virginia | High | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. The brgy. appears to lie on top of an old landslide deposit. The eastern side of the barangay is bounded by very steep slopes that have high susceptibility to landslide. This makes the brgy. also highly susceptible to landslide. The very steep slope bounding the eastern side of the brgy. is being utilized for farming, the activity of which could loosen the soil and lead to landsliding. |
| 16 | Mauno | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Intao on geohazard situation. Debris slide at Lutak and Trangban. |
| 17 | Paningayan | High (accumulation zone) | The area is situated on a landslide accumulation zone. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Constant communication and updates with Brgy. Santiago on geohazard situation. Activate BDCC. |
| 18 | Maybunga | Moderate to high | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for flood hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Identify relocation site for residents living at the foot the mountain. Avoid settlement at the foot of the slope. Mountains bounding the barangay have high susceptibility to landslide. |
| 19 | Pascuala | Moderate to high | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Tibakan on geohazard situation. Activate BDCC. |
| 20 | Lupa-an | Low to Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 21 | Oloc | Low to Moderate | Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. |
| 22 | Intao | Moderate | Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Mauno on geohazard situation. |
| 23 | Jaguiquican | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 24 | Jinalinan | Moderate | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Constant communication and updates with Brgy. Lactudan on geohazard situation. Consider relocating chapel & brgy. hall. |
| 25 | Omlot | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system for landslide hazard. Identify evacuation site. |
| 26 | Tigunhao | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system for landslide & flashflood hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Activate BDCC. |
| 27 | Maria | Moderate (Brgy. Proper); High (portions of the brgy. on accumulation zone) | The area is surrounded by steep slopes with active and recent landslides. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 28 | Casit-an | Low (Brgy. Proper); High (Purok 5) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 29 | Igtadiao | Low (Brgy. Proper); Moderate (Elevated portions) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Observe for saturated ground or seeps in areas that are not typically wet. Develop an early warning device/system. |
| 30 | Lugta | Low in the Barangay proper and Purok 4 | Observe for presence of mass movement (landslide, tension cracks) in the barangay proper and Purok 4. Develop an early warning device/system for flood hazard. Identify safe evacuation site. |
| 31 | Lactudan | Low | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Constant communication and updates with Brgy. Jinalian and Lupa-an on geohazard situation. Consider relocating school & day care center. |
| 32 | Bagongbayan | Low (Brgy. Proper); Moderate (Purok 4) | Observe for presence of mass movement (landslide, tension cracks) in Puroks 1& 4. |
| 33 | Guimbanga-an | Low | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 34 | Cadajug | None at the Barangay Proper; Moderate at Puroks 3, 4 and 5 | Observe for presence of mass movement (landslide, tension cracks) in Puroks 3,4 & 5. |
| 35 | Lindero | None (Brgy. Proper); Moderate (Sitio Malawmawan) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) in Sitio Malawmawan. |
| 36 | Guisijan | None (Brgy. Proper); Moderate (for Gaway-Gaway & Mangibo) | Observe for presence of mass movement (landslide, tension cracks) in Gaway-Gaway South and Mangibo. Develop an early warning device/system for flood & landslide hazards. |
| 37 | Liya-Liya | None (Brgy. Proper); High (Purok 2 &3) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify safe evacuation site. Tension cracks are present in Purok 3. |

In terms of flood susceptibility, thirty-seven (37) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the Thirty-seven (37) Barangays

| Barangay | Remarks/ Recommendations |
| --- | --- |
| 1 | Bagongbayan | Flooding is confined to river channels. The coastal portions of the barangay are prone to storm surge and coastal erosion. |
| 2 | Banban | Coastal erosion and storm surge. Rare flooding with depth of greater than 1m. |
| 3 | Bongbongan | None |
| 4 | Cabariwan | Flashflood with moderate turbidity is common. Sheet flooding depth greater than 1 m during rainy season. Coastal flooding. |
| 5 | Cadajug | Identify relocation site for residents living at coastal area affected by coastal erosion. |
| 6 | Canituan | None |
| 7 | Capnayan | Flash flood with high turbidity is common. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 8 | Casit-an | Flashflood with moderate turbidity is common. Sheet flooding depth 0.5-1 m during rainy season. River bank erosion along Cairawan river extensive. |
| 9 | Guimbanga-an | Sheet flooding depth greater than 1 m. Flash flood with high turbidity is common. There are70 houses affected by flooding with depth of more than a meter that can last up to 1 day. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Paliwan and Paningawan Creeks. Avoid build-up along Paliwan creek. The area is a flashflood exit point. |
| 10 | Guisijan | Coastal erosion and storm surge affect some Puroks. |
| 11 | Igtadiao | None |
| 12 | Intao | Flashflood with moderate turbidity is rare. Sheet flooding depth is 0-0.5m. Coastal erosion. |
| 13 | Jaguiquican | Flashflood with very high turbidity is very common along Paliwan River. There were at least 5 houses that were totally damaged by Typhoon Frank. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living along Paliwan River. |
| 14 | Jinalinan | Sheet flooding depth is less than 0.5m. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 15 | Lactudan | Sheet flooding depth is less than 0.5m. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 16 | Latasan | Sheet flooding depth is 0.5 - 1m. Flashflood with very high turbidity is very common. |
| 17 | Laua-an | Sheet flooding with depth of greater than 1m is rare. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 18 | Leon | Flashflood with very high turbidity is very common. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). The barangay is situated along a flashflood path. |
| 19 | Liberato | Flashflood with high turbidity is common. |
| 20 | Lindero | Sheet flooding depth is less than 0.5m for Puroks 1,2,5 & 6; greater than 1m for Puroks 3 and 4. Develop an early warning device/system for flood hazard. Identify relocation site for residents living at houses near coast affected by coastal erosion. |
| 21 | Liya-Liya | The barangay proper is susceptible to coastal flooding and river flooding along Cairawan River. Sheet flooding depth is greater than 1m. |
| 22 | Lugta | Sheet flooding depth of 0.5-1 m due to overflowing of Paliwan River affects the barangay proper. Monitor areas proximal to Paliwan River during heavy and continuous rains. |
| 23 | Lupa-an | Flashflood with moderate turbidity is common. |
| 24 | Maria | Flashflood with very high turbidity is very common. Seasonal flooding with depth of greeter than 1 m. Develop an early warning device/system for flood-related hazards. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content) along Paningayan River. Avoid build-up on Purok 3 along creek/river. |
| 25 | Mauno | Flashflood with high turbidity is rare. Sheet flooding depth greater than 1 m. |
| 26 | Maybunga | Sheet flooding depth greater than 1 m affecting rice fields. Avoid settlement adjacent to the creek. |
| 27 | Necesito | Flashflood with low turbidity is rare. |
| 28 | Oloc | Flashflood with moderate turbidity is common. Sheet flooding depth is 0.5-1 m during rainy season. Develop an early warning device/system for flood hazard. Identify safe evacuation site. Purok 4,5,6,7 are prone to coastal flooding, coastal erosion and storm surge. |
| 29 | Omlot | Sheet flooding depth is greater than 1m. |
| 30 | Pandanan | Flooding affects mainly the rice fields. Sheet flooding depth is greater than 1 m. |
| 31 | Paningayan | The barangay is on a flashflood exit point. The area can possibly be hit by the flashflood directly - the barangay proper situated on the flashflood path. Develop an early warning device/system for flashflood. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content) along Paningayan River. The residents also experience seasonal sheet flooding with depth of more than 0.5m |
| 32 | Pascuala | None |
| 33 | Poblacion | Flashflood with moderate turbidity is rare. Sheet flooding depth is 0-0.5m. Twenty houses located near the bank of Laua-an river affected by bank scouring/erosion. |
| 34 | Santiago | Flashflood with very high turbidity is very common along Tibakan Creek. Develop an early warning device/system for flashflood hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Avoid residing along creeks. Five houses along Tibakan Creek may be affected by flashflood. |
| 35 | Tibacan | Flashflood with very high turbidity is very common in the area. |
| 36 | Tigunhao | Flashflood with very high turbidity is very common in the area. Riverbank Erosion is also common in the area. Sheet flooding depth is 0.5-1m. |
| 37 | Virginia | None |

VIII.  LIBERTAD

The result of the field assessment is as follows:

- There are five (5) barangays with high landslide susceptibility (Cudiong, Igcagay, Pucio, Paz and Tinigbas)

- There are two (2) barangays with moderate landslide susceptibility (Inyawan and Tinundungan)

- There are three (3) barangays with low landslide susceptibility (Union, Lindero and San Roque)

- There are nine (9) barangays with no landslide susceptibility.

Table 1. Results of landslide assessment of the nineteen (19) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Cudiong | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and updates with the Barangay Inyawan on geohazard situation. Centro of barangay has landslide, 1 ha. of mass movement. |
| 2 | Igcagay | High | The area is on a footslope surrounded by mountains with steep slopes. The area is on a possible accumulation zone. Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for sunken or displaced road surfaces. |
| 3 | Pucio | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Tinigbas on geohazard situation. Rock slide and debris slide occur along the road. The barangay proper is situated at the footslope of a mountain with steep slope composed of highly fractured rocks and near the coast. The fractures of the rocks are dipping towards the road. |
| 4 | Paz | High | Area is on a footslope surrounded by very steep slopes. The tension cracks and other indicators of mass movement is hardly noticed by the residents due to thick vegetation. Observe for presence of mass movement (e.g. landslides, tension cracks.) |
| 5 | Tinigbas | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and upddates with the Barangays Union and Pocio on geohazard situation. The barangay proper is located at the foot of mountan with steep slope underlain by highly fractured rocks. The fractures of the rock are dipping towards the road. Moreover, the barangay proper is situated near the coast. |
| 6 | Inyawan | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and udates with Barangays Panangkulon and Cudiong on geohazard situation. |
| 7 | Tinundungan | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and upddates with the Barangay LIndero on geohazard situation. |
| 8 | Union | Low for barangay proper; Sitos Banganay and Buntawan highly susceptible to rockfall | For Sitios Banganay and Buntawan: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and upddates with the Barangay Lindero on geohazard situation. Rockfall occurs at Sitios Banganay and Buntawan. Terracets at Sitio Dulangan. |
| 9 | Lindero | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 10 | San Roque | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 11 | Barusbus | None - Barangay Proper; High - on mountainous areas. | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) Observe for sunken or displaced road surfaces. Constant communication and updates with BDCC on geohazard situation of Sitio Idiayan. Activate BDCC. |
| 12 | Panangkilon | None - Brgy. Proper; High - on mountainous areas. | Recent landslide occurences affect the agricultural land. Observe for presence of mass movement (e.g. landslides, tension cracks.) Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 13 | Tabok | None; but high for the steeply sloping mountain in the vicinity of the barangay | For the mountains bounding the barangay: monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Centro Oeste on the geohazard situation. |
| 14 | Bulanao | None |  |
| 15 | Centro East | None |  |
| 16 | Centro West | None |  |
| 17 | Cubay | None |  |
| 18 | Maramig | None |  |
| 19 | Pajo | None |  |

In terms of flood assessment, there are fifteen (15) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the nineteen (19) barangays

|  | Barangay | Remarks/Recommendation |
| --- | --- | --- |
| 1 | Barusbus | Seasonal flooding with depth of less than 0.5m. Identify evacuation site for Sitio Idiayan (prone to storm surge). Other coastal sitios can be affected by storm surge. Identify evacuation site for residents of Sitio Idiayan |
| 2 | Bulanao | Flooding only confined in fields close to Bulanao River. Possible affected sitios are Baliganay and Burbangko. Sheet flooding depth is less than 0.5m. |
| 3 | Centro East | Seasonal flooding with depth of less than 0.5m. Flashflood is very common with high turbidity. Develop an early warning device/system for flood hazard. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Area is on the river mouth and makes it highly susceptible to flashflood & debris flow. |
| 4 | Centro West | Seasonal flooding with depth of more than 1m. Flashflood is very common with high turbidity along Iniawan River. Identify evacuation site for residents along coast. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and updates with upland barangays on geohazard situation. Area is susceptible to debris flow and storm surge. |
| 5 | Cubay | Brgy. Proper is prone to storm surge; sheet flooding depth more than 1 m at Sitio Igtoog, Malikaya, and areas close to Suba River. |
| 6 | Cudiong | Seasonal sheet flooding depth is greater than 1m. |
| 7 | Igcagay | Flashflooding is rare with low turbidity. Purok 3 is highly susceptible to storm surge. Identify evacuation site for residents on coastal sitios/puroks. |
| 8 | Inyawan | Bank scouring along Inyawan River. Sheet flooding depth is greater than 1m. |
| 9 | Lindero | None |
| 10 | Maramig | None |
| 11 | Pajo | None |
| 12 | Panangkilon | Seasonal flooding with depth of more than 0.5m. Flashflood is common with moderate turbidity. Develop an early warning device/system for flood hazard. River erosion along Tamarog, Iniawan, and Kudyong Rivers affecting the ricefields. Avoid build-up along creeks. |
| 13 | Pucio | Flashflood with high turbidity is rare. Storm surge and coastal flooding. Rare occurrence of sheet flooding with depth of less than 0.5m. |
| 14 | San Roque | Flood occurs in town proper when water from river and high tide meet. Sheet flooding depth is 0.5-1m. |
| 15 | Paz | Seasonal flooding with depth of more than 0.5m. Develop an early warning device/system for flood hazard. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Storm surge on coastal puroks/ sitios. Purok 1 & 2 with at least 4 houses to be affected by flood when Kawayan Creek, Lagun-a Creek & Purok 3-4 Creek overflow. |
| 16 | Tabok | Flashflood with moderate turbidity is rare. Rare occurrence of sheet flooding with depth of 0.5-1m. |
| 17 | Tinigbas | None |
| 18 | Tinundungan | Flashflood with moderate turbidity is rare. |
| 19 | Union | Flashflood with moderate turbidity is rare. Coastal erosion, storm surge and coastal flooding also affect the barangay. Rare occurrence of sheet flooding with depth of less than 0.5m. |

IX.  PANDAN

The result of the MGB Rapid Field Assessment is as follows:

- There are four (4) barangays with high landslide susceptibility (Badiangan, Luhod-Bayang, Perfecta, Patria)

- There are four (4) barangays with moderate landslide susceptibility (Aracay, Candari, San Joaquin, Idiacacan)

- There are nine (9) barangays with low landslide susceptibility (Talisay, Buang, Cabugao, Duyong, Fragante, Tingib, Santa Ana, Sta. Cruz, Nauring)

- There are fifteen (15) barangays with no landslide susceptibility.

- Barangays Maadios, and Napuid were not assessed due to poor weather condition and difficulty of access during the time of the survey.

Table 1. Results of Landslide Assessment of the thirty-two (32) Barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Badiangan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device system for landslide. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living at the foot of the mountain (southern portion of) bounding Sitio Batiw (Purok 4) and Centro (Purok 1 & 2). Constant communication and updates with Brgy. Perfecta on geohazard situation. Activate BDCC. |
| 2 | Luhod-Bayang | High | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Patria on geohazard situation. Activate Barangay disaster Coordinating Council (BDCC). Sitio Hinugtan and Bayang areas with landslide occurrences. |
| 3 | Perfecta | High | Monitor progress of mass movement (landslide, tension cracks). Observe for presence of mass movements; (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flashflood hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation sites for residents living at Brgy. Perfecta.Relocation of residents living adjacent to the river (Purok 2) is immediately needed. Constant communication and updates with Brgy Sta. Ana on geohazard situation. Activate BDCC. Get rid of tress within the Garot River and Panukuyan River. |
| 4 | Patria | High | Monitor Progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangays Luhod-bayang and Duyong on geohazard situation. Soil slide occurs at Sitio Tabay. |
| 5 | Aracay | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) |
| 6 | Candari | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Duyong on geohazard situation (recent rockfall escarpments observed at Mt. Mab-O at Barangay Duyong). |
| 7 | San Joaquin | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device system for landslide. Identify new evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living at Purok 5. Constant communication and updates with Brgy. Sta. Ana on geohazard situation. Activate BDCC. |
| 8 | Idiacacan | Moderate at the Barangay Proper and Purok 5 | Observe for presence of mass movements (e.g. landslides, tension cracks) at the barangay proper and at Purok 5. |
| 9 | Talisay | Low (Brgy. Proper); Moderate (Purok Har-aw) moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for sunken or displaced road surfaces. |
| 10 | Buang | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for sunken or displaced road surfaces. |
| 11 | Cabugao | Low | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 12 | Duyong | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Activate Barangay Disaster Coordinating System (BDCC). |
| 13 | Fragante | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 14 | Tingib | Low | Monitor Progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living along the coastline. Constant communication and upddates with the Barangay Mag-aba on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). Sitio Montile is a possible landslide area. |
| 15 | Santa Ana | Low (Brgy. Proper); High (Purok Matutum) | Monitor progress of mass movement (landslide, tension cracks). Observe for presence of mass movements; (e.g. landslides, tension cracks). Develop an early warning device system for landslide. Identify evacuation site.Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. Identify relocation site for residents living at Purok Matutum. Constant communication and updates with Brgy. San Joaquin on geohazard situation. Activate BDCC. |
| 16 | Santa Cruz | Low (Brgy. Proper); High (Sitio Pagapawan) | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 17 | Nauring | None to low | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 18 | Baybay | None |  |
| 19 | Botbot | None | Observe for presence of mass movements (e.g. landslides, tension cracks) in Mount Intangasan. |
| 20 | Carmen | None |  |
| 21 | Centro Norte (Pob.) | None |  |
| 22 | Centro Sur (Pob.) | None |  |
| 23 | Dionela | None |  |
| 24 | Guia | None | Sitio Tuburan, Malumpati and Calaylay are upland areas where occurrences of landslide are possible. Recommendation for upland areas : Observe for presence of mass movements (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Jinalin on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 25 | Jinalinan | None | One sitio with low landslide rating. Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 26 | San Andres | None | Observe for presence of mass movements; (e.g. landslides, tension cracks). |
| 27 | Mag-aba | None | Sitio Puke and Tigawon are possible landslide areas. Monitor Progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and upddates with the Barangays Sto. Rosario and Tingib on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 28 | Sto. Rosario | None | Sitio Pangdan, Tuburan, Calaylay, Ipil and Bingawan are landslide areas. For these sitios, recommendations are: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces.Constant communication and upddates with Barangays Jinalin and Zaldivar on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 29 | Zaldivar | None |  |
| 30 | Bagumbayan | None (Brgy. Proper); Low (Purok 6) | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Purok 6 (some houses are located footslopes). |
| 31 | Santa Fe | None at the barangay proper and high at portions of Mount Bugtong Buto. | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. |
| 32 | Dumrog | None at the Barangay Proper and moderate at Puroks 1, 3 and Sitio Bura | Monitor progress of mass movement (landslide, tension cracks) in Puroks 1 and 3. Observe for presence of mass movements; (e.g. landslides, tension cracks) in other portions of the barangay. Develop an early warning device/system. Identify evacuation site. |
| 33 | Maadios | Not assessed due to difficulty in accessing the area |
| 34 | Napuid | Not assessed due to difficulty in accessing the area |

In terms of flood susceptibility, thirty-two (32) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the thirty-two (32) Barangays

|  | Barangay | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Aracay | None |
| 2 | Badiangan | Flashflood with very high turbidity is very common in the area. Develop an early warning device system for flashflood. Debris (including fallen trees) in the Panukayan River must be cleared as this could cause damming of the river (and consequently, the occurrence of flashflood) particularly during typhoon or heavy, continuous rains. River erosion affects Sitio Batiw.Avoid settlement near the river. |
| 3 | Bagumbayan | Seasonally flooded with depth more than 1 meter. Flashflood with very high turbidity affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning device/system for flood-related hazard. Identify evacuation site. Identify relocation site for residents living at Purok 3 (prone to coastal flooding). Constant communication and updates with Barangay Fragante on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 4 | Baybay | Low-lying areas are seasonally flooded with depth 0.5-1 meter. Storm surge also affects the area. |
| 5 | Botbot | The barangay proper, Puroks 4, 5 and 9 are seasonally flooded with depth 0-0.5 meter. |
| 6 | Buang | Seasonally flooded with depth more than 1 meter. Flashflood with very high turbidity commonly affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Nauring River. Erosion along Buang Creek affects plantations. |
| 7 | Cabugao | Seasonally flooded with depth more than 1 meter. Flashflood with very high turbidity commonly affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Houses located near Talisay-Cabugao River highly susceptible to flooding. Identify evacuation and/or relocation site for the residents. |
| 8 | Candari | Seasonally flooded with depth more than 1 meter. Flashflood with moderate turbidity commonly affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living at Sitio Tubkan located near Malumpati River and houses located near Colanos Creek. |
| 9 | Carmen | The barangay proper and Purok 3 are seasonally flooded with depth 0.5-1 meter. Puroks 1 and 4 are seasonally flooded with depth 0-0.5 meter. Flashflood with low turbidity is rare. Develop an early warning device/system. Identify evacuation site. Flooding is mainly due to the overflowing of Cabilauan River. |
| 1 | 0 Centro Norte (Pob.) | The barangay proper, Puroks 4 and 6 are seasonally flooded with depth 0-0.5 meter. Puroks 1 and 2 are seasonally flooded with depth 0.5-1 meter. Purok 3 and 7 are seasonally flooded with depth more than 1 meter. Develop an early warning device/system. |
| 1 | 1 Centro Sur (Pob.) | The barangay proper, Purok 6 and 7 are seasonally flooded with depth 0.5-1 meter. Puroks 2,3,4 and 5 are seasonally flooded with depth 0-0.5 meter. Develop an early warning device/system. Identify evacuation site. |
| 1 | 2 Dionela | Seasonally flooded with depth greater than 1 meter. Identify safe evacuation site. |
| 1 | 3 Dumrog | No flood susceptibility in barangay proper. Purok 1 and 3 are seasonally flooded with depth 0-0.5 meter. Coastal areas are affected by storm surge. |
| 1 | 4 Duyong | Rare occurrence of flood with depth 0-0.5 meter. Flashflood with low turbidity is rare. Coastal areas are affected by storm surge. |
| 1 | 5 Fragante | Seasonally flooded with depth more than 1 meter. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living at Sitio Sabay located near Nauring River. |
| 1 | 6 Guia | Seasonally flooded with depth more than 1 meter. Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Jinalin on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 1 | 7 Idiacacan | Puroks 2, 4, 6 and 7 are affected by storm surge. Identify evacuation site for residents during stormy conditions. |
| 1 | 8 Jinalinan | Seasonally flooded with depth more than 1 meter. Flashflood with moderate turbidity is very common. Coastal areas are affected by storm surges |
| 1 | 9 Luhod-Bayang | Seasonally flooded with depth more than 1 meter. Flashflood with moderate turbidity is common. River passes at the barangay proper. Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
|  | 20 Maadios | Not assessed due to difficulty in accessing the area |
|  | 21 Mag-aba | Rare occurrence of flood with depth greater than 1 meter. Flashflood with low turbidity is rare. Coastal areas are affected by storm surges and erosion. Identify relocation site for those affected by coastal erosion. Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
|  | 22 Napuid | Not assessed due to difficulty in accessing the area |
| 2 | 3 Nauring | Seasonally flooded with depth 0.5-1 meter. Identify relocation site for residents living at Purok 1 and 2 located near the coast (highly susceptible to coastal flooding and storm surge). Identify evacuation site for families affected by flood. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Constant communication and updates with Barangay Bagumbayan on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 2 | 4 Perfecta | Seasonally flooded with depth more than 1 meter. FlashFlood accompanied by debris flow is very common in the area affecting the Panukuyan River and Garut River. |
| 2 | 5 San Andres | Dangkalan, Ipil, Mahogany and Avocado seasonally flooded with depth 0-0.5 meter. Narra seasonally flooded with depth 0.5-1 meter. Erosion along Panuktukan river. Avoid building houses adjacent to the river. |
| 2 | 6 San Joaquin | Seasonally flooded with depth more than 1 meter. Develop an early warning device system for flashflood.Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Identify relocation site for residents living at Purok 6 or houses lie on an active floodplains. |
| 2 | 7 Santa Ana | Seasonally flooded with depth more than 0-0.5 meter.Develop an early warning device system for flashflood.Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Relocate houses on floodplain areas. |
| 2 | 8 Santa Cruz | Seasonally flooded with depth 0.5-1 meter. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 2 | 9 Santa Fe | Puroks 1, 2 and 3 have moderate flood susceptibility due to the overflowing of creeks and rivers; Coastal flooding, storm surge, coastal erosion also affect the area. |
|  | 30 Talisay | Seasonally flooded with depth more than 1 meter. Flashflood with very high turbidity affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
|  | 31 Patria | Rare occurrence of flood with depth 0.5-1 meter. Flashflood with moderate turbidity is rare. |
|  | 32 Sto. Rosario | Seasonally flooded with depth more than 1 meter. Flashflood with moderate turbidity is common. Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces.Constant communication and upddates with Barangays Jinalin and Zaldivar on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
|  | 33 Tingib | Rare occurrence of flood with depth 0-0.5 meter. Coastal areas are affected by storm surges and erosion. Identify relocation site for those affected by coastal erosion. Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
|  | 34 Zaldivar | Seasonally flooded with depth more than 1 meter. Flashflood with high turbidity is very common. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and upddates with Barangay Jinalinan on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |

X. PATNONGON

The result of the MGB Rapid Field Assessment is as follows:

- There are twenty-one (21) barangays with high landslide susceptibility (Alvañiz, Badiangan, Bitas, Cuyapiao, Igbobon, La Rioja, Macarina, Pandanan, Salaguiawa, Samalague, Tobias Fornier, Villa Cruz, Villa Elio, Villa Laua-an, Villa Sal, Villa Salomon, San Rafael, Gella, Igburi, Villa Crespo, Vista Alegre).

- There are five (5) barangays with moderate landslide susceptibility (Tamayoc, Patlabawon, Villa Flores, Tigbalogo, Quezon)

- There are ten (10) barangays with no landslide susceptibility.

Table 1. Results of Landslide Assessment of the thirty-six (36) Barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Alvañiz | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flood hazards. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Relocate Barangay Alvañiz (the whole barangay is located at the foot of a mountain where gullies and old landslide escarpments were observed). Constant communication and updates with Barangay Quezon on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 2 | Badiangan | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at 2 houses at the foot of the landslide (Igtuba). Constant communication and updates with the Barangay Pandanan on geohazard situation. Landslide at Igtuba. |
| 3 | Bitas | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flood hazards. Identify evacuation site. Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Relocate Barangay Bitas (the whole barangay is located at the foot of a mountain range where gullies, recent landslide escarpments and triangular facets were observed). Constant communication and updates with Barangay Gen. Luna on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 4 | Cuyapiao | High | Observe for presence of mass movement (e.g. landslides, tension cracks). Consider looking for relocation site |
| 5 | Igbobon | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Tension cracks at Sitio Tacas wherein more than 15 houses is located. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Poblacion on geohazard situation. |
| 6 | La Rioja | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Igbobon on the geohazard situation. Landslide occur at Rosa Mistica mountain. |
| 7 | Macarina | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Pandanan on geohazard situation. Landslide occurs at Ipilipis area, Tarangbang and Agak. |
| 8 | Pandanan | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at landslide prone areas earlier identified by MGB Reg VI and for those living adjacent to the Carit-an River and Coronapan Creek. landslide prone areas. Constant communication and updates with the Barangay Badiangan on geohazard situation. Have the proposed relocation site be assessed by MGB, DENR-6 for its suitability letter addressed to Engr. Leo Van V. Juguan OIC, Regional Director MGB-6, Iloilo City Tel. (033) 3362815. 2007 MGB-6 personnel have investigated occurrence of landslide in the area and 12 houses were advised to relocate. |
| 9 | Salaguiawan | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Observe for sunken or displaced road surfaces. |
| 10 | Samalague | High | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content).Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Badiangan on geohazard situation. |
| 11 | Tobias Fornier | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flood hazards. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Purok 2 (located at the foot of a mountain where gullies and old landslide escarpments were observed). Relocate Day Care Center, Chapel and Barangay Hall (located at the foot of a creeping slope) and T. Fornier Primary School (highly susceptible to flood). Constant communication and updates with Barangay Gen. Luna, Carmelo 1 and 2, and Buga on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 12 | Villa Cruz | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangays Pandanan and Carit-an on geohazard situation. Occurrence of landslide in the mountains of the barangay in 2007. Houses located near the banks of the river should always be vigilant during typhoons or continous rains. |
| 13 | Villa Elio | High | Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. |
| 14 | Villa Laua-an | High | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for sunken or displaced road surfaces. |
| 15 | Villa Sal | High | Observe for sunken or displaced road surfaces.,consider looking for relocation site of school |
| 16 | Villa Salomon | High | Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for sunken or displaced road surfaces. |
| 17 | San Rafael | High at the barangay proper, Purok 1, 2 and 3 | Monitor progress of mass movement (e.g. landslides, tension cracks) in the entire barangay. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for flood , flashflood and landslide hazards. Identify safe evacuation site. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Patlabawon on flashflood situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 18 | Gella | Moderate to high | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site.Develop an early warning device/system for landslide Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Gella 2. Constant communication and updates with the Barangay Tigbalogo on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 19 | Igburi | Moderate to high | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 20 | Villa Crespo | Moderate to high | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 21 | Vista Alegre | Moderate to high | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Gen. Luna on geohazard situation. The whole barangay is located on the mid-slope where creeping was observed. Relocate Vista Alegre Elementary School and San Roque Chapel (located at the foot of a slope where recent landslide escarpments were observed). Activate Barangay Disaster Coordinating Council (BDCC). |
| 22 | Tamayoc | Moderate | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated group or seeps in areas that are not typically wet. |
| 23 | Patlabawon | Moderate | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. |
| 24 | Villa Flores | Moderate at barangay proper and high for mountains/slopes bounding it. | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks).Constant communication and updates with the Barangay Villa Sal on geohazard situation. Avoid putting up any structure at the foot of the slopes bounding the barangay proper as they are highly susceptible to landslide. A number of landslides have been noted, but only affecting ricefields. |
| 25 | Tigbalogo | Moderate to barangay proper and High to Purok 1. | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslideand flashdlood. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increase turbidity (soil content). Observe for saturated group or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Purok 1.Activate Barangay Disaster Coordinating Council (BDCC). |
| 26 | Quezon | Moderate to barangay proper and High to slope boundary. | Monitor progress of mass movement(e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Stay away from the foot of the mountains bounding the barangay proper as they are highly susceptible to landslide. |
| 27 | Amparo | None |  |
| 28 | Carit-an | None |  |
| 29 | Igbarawan | None |  |
| 30 | Mabasa | None |  |
| 31 | Magarang | None |  |
| 32 | Magsaysay | None |  |
| 33 | Padang | None |  |
| 34 | Poblacion | None |  |
| 35 | Apgahan | None at the barangay proper; Moderate at Puroks 5; Low in Purok 2 | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. |
| 36 | Aureliana | None at the barangay proper; Moderate at Puroks 6; Low in Purok 2 | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. |

In terms of flood susceptibility, thirty-six (36) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the thirty-six (36) Barangays

|  | Barangay | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Alvañiz | Seasonally flooded with depth greater than 1 meter. Flashflood commonly affects the area during rainy season. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increased turbidity (soil content). Relocate Magranting Primary School and houses located near Ipayo River. |
| 2 | Amparo | Seasonally flooded with depth 0.5-1 meter. |
| 3 | Apgahan | Seasonally flooded with depth of 0-0.5 meter in Puroks 3 and 6. Low lying areas are flooded (low flood susceptibility due to improper drainage). Coastal areas are affected by storm surge. |
| 4 | Aureliana | Flooding in low-lying areas of Purok 3 are due to improper drainage. Purok 7 is affected by coastal flooding and storm surge. River scpuring along Aureliana River also affects the area. |
| 5 | Badiangan | Rare occurrence of flood with depth 0.5-1 meter. Riverbank scouring/erosion also a problem; Twenty houses are located near the bank of the river. Consider relocating the houses. |
| 6 | Bitas | Seasonally flooded with depth greater than 1 meter. Flashflood with moderate turbidity affects the area. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increased turbidity (soil content) along Bitas River, Yabangan Creek, Tigwang Creek and Igbakan Creek. |
| 7 | Carit-an | Seasonally flooded with depth greater than 1 meter. |
| 8 | Cuyapiao | None |
| 9 | Gella | Flashflood with very high turbidity is very common. |
|  | 10 Igbarawan | Seasonally flooded with depth greater than 1 meter. Riverbank erosion observed in the area. |
|  | 11 Igbobon | Rare occurrence of flood with depth greater than 1 meter. Flashflood with moderate turbidity is rare. |
|  | 12 Igburi | None |
|  | 13 La Rioja | Seasonally flooded with depth of 0.5-1 meter. Flashflood with moderate turbidity is rare. |
|  | 14 Mabasa | Seasonally flooded with depth 0-0.5 meter. |
|  | 15 Macarina | Rare occurrence of flood with depth greater than 1 meter. |
|  | 16 Magarang | None |
|  | 17 Magsaysay | Rice fields are affected during high tide. Three households are affected by Aurelliana river overflow (moderate flood susceptibility). Develop an early warning device/system for flood-related hazard. |
|  | 18 Padang | Seasonally flooded with depth 0-0.5 meter. Develop an early warning device/system. Houses located near the shore are affected by storm surge. |
|  | 19 Pandanan | Rare occurrence of flood with depth 0.5-1 meter. Flashflood with moderate turbidity is rare. |
|  | 20 Patlabawon | None |
|  | 21 Poblacion | Erosion along Ipayo river. Tigmanali creek overflow affecting houses situated near the banks of Tigmanali creek. |
|  | 22 Quezon | Riverbank erosion is a potential problem. Avoid settlement near the bank of the river. |
|  | 23 Salaguiawan | None |
|  | 24 Samalague | Seasonally flooded with depth greater than 1 meter. Flash flood with moderate turbidity is common. |
|  | 25 San Rafael | Flashflood with high turbidity is very common. |
|  | 26 Tamayoc | Seasonally flooded with depth 0.5-1 meter. |
|  | 27 Tigbalogo | Flashflood is very common in the area. |
|  | 28 Tobias Fornier | Seasonally flooded with depth greater than 1 meter. Flashflood with moderate turbidity affects the area. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increased turbidity (soil content). Relocate T. Fornier Primary School (highly susceptible to flood). |
|  | 29 Villa Crespo | None |
|  | 30 Villa Cruz | Rare occurrence of flood with depth 0.5-1 meter. |
|  | 31 Villa Elio |  |
|  | 32 Villa Flores | Avoid settlement near the bank of the river as bank erosion could be a problem |
|  | 33 Villa Laua-an | None |
|  | 34 Villa Sal | None |
|  | 35 Villa Salomon | None |
|  | 36 Vista Alegre | Seasonally flooded with depth 0.5-1 meter. Observe for rapid increase/decrease in creeks/river water levels, possibly accompanied by increased turbidity (soil content) along Atabay and Igtulo Creeks. |

XI.  SAN JOSE

The result of the field assessment is as follows:

- There are four (5) barangays with low landslide susceptibility (Barangay 1, Cansadan, Igbonglo, Pantao and San Pedro)

- There are twenty-four (23) barangay centers with no landslide susceptibility.

Table 1. Results of landslide assessment of the twenty-eight (28) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Barangay 1 (Pob.) | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 2 | Cansadan (Cansadan-Tubudan) | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 3 | Igbonglo | Low | Soil creeping observed along the roads going to Brgy.Pantao. Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 4 | Pantao | Low | Soil creeping observed in the area. Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 5 | San Pedro | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 6 | Atabay | None |  |
| 7 | Badiang | None |  |
| 8 | Barangay 2 (Pob.) | None |  |
| 9 | Barangay 3 (Pob.) | None |  |
| 10 | Barangay 4 (Pob.) | None |  |
| 11 | Barangay 5 (Pob.) | None |  |
| 12 | Barangay 6 (Pob.) | None |  |
| 13 | Barangay 7 (Pob.) | None |  |
| 14 | Barangay 8 (Pob.) | None |  |
| 15 | Bariri | None |  |
| 16 | Bugarot (Catungan-Bugarot) | None |  |
| 17 | Durog | None |  |
| 18 | Funda-Dalipe | None |  |
| 19 | Inabasan | None |  |
| 20 | Madrangca | None |  |
| 21 | Magcalon | None |  |
| 22 | Malaiba | None |  |
| 23 | Maybato Norte | None |  |
| 24 | Maybato Sur | None |  |
| 25 | Mojon | None |  |
| 26 | San Angel | None |  |
| 27 | San Fernando | None |  |
| 28 | Supa | None |  |

In terms of flood assessment, there are twenty-one (21) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the twenty-eight (28) barangays

|  | Barangay | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Atabay | Seasonal flooding with depth of more than 1m. Drainage canals inappropriate; not able to accommodate drains/wastewaters. |
| 2 | Badiang | None |
| 3 | Barangay 1 (Pob.) | Seasonal flooding with depth of less than 0.5m. Barangay inundated due to the overflowing of the swimming pool near the post office especially during continuous heavy rains. |
| 4 | Barangay 2 (Pob.) | Seasonal flooding with depth of less than 0.5m. Observe for increase in flood water depth and duration of flood. |
| 5 | Barangay 3 (Pob.) | Seasonal flooding with depth of less than 0.5m. Flood duration can last for half-day up to 4 days. Keep records of flooding incidents. |
| 6 | Barangay 4 (Pob.) | The barangay proper affected by storm surge, sheet and coastal flooding with depth of 0.5 to 1 meter. The rest of the barangay is also affected by coastal flooding and storm surge. |
| 7 | Barangay 5 (Pob.) | None |
| 8 | Barangay 6 (Pob.) | Low flooding with depth of less than 0.5m. Flooding is mainly due to drainage problem. |
| 9 | Barangay 7 (Pob.) | None |
| 10 | Barangay 8 (Pob.) | Purok Tinapok is regularly flooded during heavy and continuous rainfall due to insufficient drainage. Purok Pigado experiences storm surge. |
| 11 | Bariri | High flooding with more than 1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify evacuation site. Constant communication and updates with Brgy. Inabasan on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 12 | Bugarot (Catungan-Bugarot) | Seasonal flooding with depth of more than 1m. Develop an early warning device/system for flood-related hazard. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living at Barangay Catungan-Bugarot. Constant communication and updates with Barangay Inabasan on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 13 | Cansadan (Cansadan-Tubudan) | None |
| 14 | Durog | Flashflood with very high turbidity is very common. Identify relocation site for residents living at Durog. Activate BDCC. The barangay proper is affected by coastal and sheet flooding with depth of greater than 1 meter. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 15 | Funda-Dalipe | Develop an early warning device/system related to storm surge problem. Storm surge a common problem affecting the areas. |
| 16 | Inabasan | Seasonal flooding with depth of more than 1m. Flashflood with high turbidity affects the area. Develop an early warning device/system for flood-related hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living at Purok 2. Constant communication and updates with Barangay Inabasan on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| 17 | Madrangca | Seasonal flooding with depth of less than 0.5m that can last for a week. Keep records of flooding in barangay proper, sitios and vicinities. |
| 18 | Magcalon | None |
| 19 | Malaiba | Storm surge is a perennial problem of the barangay. |
| 20 | Maybato Norte | Flooding in Purok 5 is due to drainage problem. |
| 21 | Maybato Sur | Purok Riverside is moderately susceptible to coastal and sheet flood with depth of 0.5 to 1 meter. The area is located east of Malandog River. Storm surge affects the barangay proper. |
| 22 | Mojon | None |
| 23 | San Angel | Seasonal flooding witrh depth of less than 0.5m. The area is affected by storm surge. |
| 24 | San Fernando | None |
| 25 | San Pedro | Flashflood with high turbidity is common. The barangay proper is susceptible to flood with depth of 0.5 to 1 meter. |
| 26 | Supa | High flooding with depth of more than 1m occurs seasonally. Evacuate or go to higher ground if province is projected to be hit by typhoon. |
| 27 | Igbonglo | None |
| 28 | Pantao | Bank scouring/erosion along Durog creek. |

XII.  SAN REMEGIO

The result of the field assessment is as follows:

- There are twenty-three (23) barangays with high landslide susceptibility (Agricula, Bulan-bulan, Cabunga-an, Carmelo II, General Luna, La Union, Lumpatan, Maragubdub, Nagbangi I (Amatong), Nagbangi II, Osorio I, Ramon Magsaysay, Tubudan, Bagumbayan, Cabiawan, San Rafael, Baladjay, Magdalena, Trinidad, Vilvar, Atabay, Bugo and Iguirindon)

- There are eight (8) barangays with moderate landslide susceptibility (Osorio II, Alegria, Aningalan, Carawisan I, Orquia (Igcatumbal), Poblacion, Sinundolan, and Lapak)

- There are four (4) barangays with low landslide susceptibility (Carmelo I, Barangbang, Carawisan II and Nasuli).

- There is one (1) barangay with no landslide susceptibility.

Table 1. Results of landslide assessment of the thirty-six (36) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Agricula | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 2 | Bulan-bulan | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide-related hazard.Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). There is an urgent need to find a relocation site for the whole Brgy. Bulan-Bulan as (1) the riverbed of Inyaman creek has aggraded/risen to a critical level (i.e. just a few meters below the brgy.); (2) the Brgy. proper is near to a mountain that has high susceptibility to landslide. It seems that the brgy. is underlain by an old landslide deposit. |
| 3 | Cabunga-an | High | Monitor progress of mass movement & observe for presence of mass movement (e.g., landslides, tension cracks). Develop an early warning device/system for landslide and flood related hazard.Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Constant communication and updates with brgy. San Rafael, Trinidad, Bugo on geohazard situation. Avoid settlement near the Cabunga-an river. Consider looking for a relocation site. |
| 4 | Carmelo II | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide-related hazard. Carmelo II Elementary School is highly susceptible to landslide. |
| 5 | General Luna | High | The intense gullying, rilling, presence of recent landslides, extremely steep slopes and presence of fault structures make the barangay proper highly susceptible to landslide. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces.Constant communication and updates with MDCC on geohazard situation. Activate BDCC. |
| 6 | La Union | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Poblacion on geohazard situation. Landslides in the barangay proper, Sitio de la Torre and Sitio Bato Inca, only farmlands are affected. Develop an early warning system/device. |
| 7 | Lumpatan | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide & flashflood.Identify evacuation site. Observe for sunken or displaced road surfaces. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Brgy. Lumpatan especially Sitio Dalugdog. Constant communication and updates with Brgy. LapakI on geohazard situation. Activate BDCC. |
| 8 | Maragubdub | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks).Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Seepages on cracks of 30 cm-1 m width were observed. Discuss possibility of relocation with constituents. BDCC contingency planning for flashflood/flooding/landslide. Inform residents of potential landslide. |
| 9 | Nagbangi I (Amatong) | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system.Identify evacuation site. Observe for sunken or displaced road surfaces. |
| 10 | Nagbangi II | High | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system.Identify evacuation site. Observe for sunken or displaced road surfaces. |
| 11 | Osorio I | High | Monitor progress of mass movement (e.g. landslides, tension cracks) Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide-related hazards. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Unstable cut slopes composed of unconsolidated materials are highly susceptible to landslides. Constant communication and updates with Brgy. Osorio II on geohazard situation. Activate Barangay Disaster Coordinating Council. |
| 12 | Ramon Magsaysay | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Observe saturated ground or seeps in areas that are not typically wet. Contingency planning for landslide threat. Record progress of cracks and inform residents living on the foot slope about rockfall/rockslide that may directly affect them. About 6 houses are in direct danger of slumping |
| 13 | Tubudan | High | Observe for presence of mass movement (landslide, tension cracks). Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. La Union on geohazard situation. Activate BDCC. Warn barangays located at the footslopes if tension cracks are observed at the ridge. |
| 14 | Bagumbayan | High - accumulation zone and steep slopes surrounding the barangay proper | Monitor progress & observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. BDCC contingency planning on flood/flashflood/debris flow hazards. Relocation site for entire brgy. had been identified already but has to be consulted with MGB for assessment. |
| 15 | Cabiawan | High - possible accumulation zone | Monitor progress of mass movement & observe for presence of mass movement (e.g., landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Tension cracks with width of 50 cm are common on the steep slopes of Cabicuran, directly affecting the brgy. proper. Inform residents of possible landslide hazards. Seepages on cracks are also common. BDCC contingency. Consider possible relocation. |
| 16 | San Rafael | High - Puroks on mountains | Barangay proper is a possible accumulation zone.Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site for Puroks Israel and Hawaii. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 17 | Baladjay | High (accumulation zone) | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flood related hazard. Constant communication & updates with MDCC on geohazard situation. Activate BDCC and inform residents on hazards of flood, flashflood and landslide. Discuss the possibility of relocation. Mudflow/debris flow on Purok Campo and Purok Durog. |
| 18 | Magdalena | High (Possible accumulation zone) | Debris flow and mudflow along Sibalom is possible. Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide & flood. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Discuss the possibility of relocation among constituents. BDCC contingency planning. |
| 19 | Trinidad | High (Possible accumulation zone) | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system intended for landslide-related hazards. Identify evacuation site.Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). BDCC contingency planning. |
| 20 | Vilvar | High (Possible accumulation zone) | Possible mudflow, debris flow and slumping can affect the barangay. Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flood related hazard. Identify evacuation site; Constant communication and updates with MDCC on geohazard situation. Activate BDCC and adopt a contingency planning for landslide and flooding. Inform residents of threats of landslides and flooding. Discuss with the constituents the possibility of relocation. |
| 21 | Atabay | High (Sitio Cangaranan, Sitio Tibanglanan) | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. |
| 22 | Bugo | High (Sitio Igbutong) | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. |
| 23 | Iguirindon | High to moderate | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks).. Identify relocation site for residents living at Purok Durog. BDCC contingency planning for landslide. |
| 24 | Osorio II | Moderate to High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide-related hazards. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Activate Barangay Disaster Coordinating Council (BDCC). |
| 25 | Alegria | Moderate at the Brgy. proper; High at Sitio Lisdo | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide-related hazard. Identify relocation site for residents living at Sitio Lisdo. Constant communication and updates with Brgy. Lumpatan, Bugo, Trinidad on geohazard situation.Several active landslide and landslide debris noted along Ingaman River. Once remobilized, these could possibly dam the river and eventually lead to flashflooding in the downstream areas (e.g. Lumpatan, Bugo, Trinidad) |
| 26 | Aningalan | Moderate | Monitor progress of mass movement (e.g. landslides, tension carcks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 27 | Carawisan I | Moderate | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Carawisan II on geohazard situation. Activate BDCC. Landslide at Sitio Caeno and cracks were observed, affecting mainly farmlands. |
| 28 | Orquia (Igcatumbal) | Moderate | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for flashflood. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Activate BDCC. |
| 29 | Poblacion | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe saturated ground or seeps in areas that are not typically wet. |
| 30 | Sinundolan | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Recent/active landslides at Sitio Bungsod. |
| 31 | Lapak | Moderate; agricultural area also prone to landslide | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide. Identify evacuation site. Observe for sunken or displaced road surfaces. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living at Sitio Canlogan. Constant communication and updates with Brgy. Lumpatan on geohazard situation. Activate BDCC. |
| 32 | Carmelo I | Low to Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide and flood hazards. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Carmelo 2 on geohazard situation. |
| 33 | Barangbang | Low | Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and updates with Brgy. Cadolonan on geohazard situation. Activate BDCC. |
| 34 | Carawisan II | Low | Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 35 | Nasuli | Low | Observe for sunken or displaced road surfaces. Landslides at the boundary with Brgy. Barangbang. |
| 36 | Cadolonan | None | Landslide in Sitio Kinabahan affected farmlands. Monitor progress of mass movement & observe for presence of mass movement (e.g. landslides, tension cracks). |
| 37 | Banbanan | Not assessed due to difficulty in accessing the area |  |
| 38 | Bawang | Not assessed due to difficulty in accessing the area |  |
| 39 | General Fullon | Not assessed due to difficulty in accessing the area |  |
| 40 | Insubuan | Not assessed due to difficulty in accessing the area |  |
| 41 | Panpanan I | Not assessed due to difficulty in accessing the area |  |
| 42 | Panpanan II | Not assessed due to difficulty in accessing the area |  |
| 43 | Rizal | Not assessed due to difficulty in accessing the area |  |
| 44 | Sumaray | Not assessed due to difficulty in accessing the area |  |
| 45 | Walker | Not assessed due to difficulty in accessing the area |  |

In terms of flood assessment, there are thirty (30) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the thirty-six (36) barangays

|  | Barangay | Remarks/Recommendation |
| --- | --- | --- |
| 1 | Agricula | None |
| 2 | Alegria | None |
| 3 | Aningalan | Seasonal flooding with depth of more than 1m. Erosion along Sambulaun Creek. Overflowing of Alakyan and Tipuluan Rivers affect plantations. |
| 4 | Atabay | Sheet flooding depth greater than 1m at Sitios Cangaranan and Tibanglanan. Flashflood rarely occurs. |
| 5 | Bagumbayan | Flashflood is very common with moderate turbidity. Seasonal sheet flooding with depth of more than 1m. Sheet flooding depth greater than 1m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Entire barangay was affected by Typhoon Frank. |
| 6 | Baladjay | Seasonal flooding with depth of less than 1m. Flashflood very common with moderate turbidity along Sibalom River. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) of Sibalom River and Pula Creek. |
| 7 | Banbanan | Not assessed due to difficulty in accessing the area |
| 8 | Barangbang | Flashflood very common with high turbidity. Sheet flooding depth greater than 1 m. Develop an early warning device/system. Identify evacuation site. Identify relocation site for residents living along Sibalom River. |
| 9 | Bawang | Not assessed due to difficulty in accessing the area |
| 10 | Bugo | Barangay a "permanent danger zone". Relocation site has to be identified by the brgy. Officials concern. Sheet flooding in the area is seasonal with depth of less than 0.5m |
| 11 | Bulan-bulan | None |
| 12 | Cabiawan | Sheet flooding depth greater than 1m. Flash flood is very common with moderate turbidity. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 13 | Cabunga-an | Flashflood commonly occurs with high turbidity affecting ricefields. Avoid settlement adjacent to the river. Sheet flooding depth greater than 1 m. |
| 14 | Cadolonan | Sheet flooding depth greater than 1m. Flash flood very common with high turbidity. Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living along Sibalom River. Constant communication and updates with Brgy. Barangbang on geohazard situation. Activate BDCC. |
| 15 | Carawisan I | Sheet flooding depth 0-0.5 m. Bank scouring/erosion present in the area. |
| 16 | Carawisan II | Flashflood very common with high turbidity. Sheet flooding occurs seasonally with depth of more than 1m. Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living along Sibalom River. Constant communication and updates with Brgy. Barangbang on geohazard situation. Activate BDCC. |
| 17 | Carmelo I | Damming along Implanog Creek can cause flashflood. Seasonal flooding with depth of less than 1m. |
| 18 | Carmelo II | Seasonal flooding withy depth of less than 1m. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Damming along Implanog Creek can cause flashflood. |
| 19 | General Fullon | Not assessed due to difficulty in accessing the area |
| 20 | General Luna | Rare occurrence of flashflood with very high turbidity |
| 21 | Iguirindon | Flashflooding is very common with moderate turbidity. Seasonal flooding with depth of less than 0.5m. Avoid build-up along Sibalom River and Libunan Creek.Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content) along Sibalom River and Libinan Creek. |
| 22 | Insubuan | Not assessed due to difficulty in accessing the area |
| 23 | La Union | None |
| 24 | Lapak | None |
| 25 | Lumpatan | Flashflood very common with high turbidity. River bank erosion also affects the area. |
| 26 | Magdalena | Flashflood very common with high turbidity. Sheet flooding depth greater than 1 m. |
| 27 | Maragubdub | Flashflood along Sibalom River is very common with moderate turbidity. Seasonal sheet flooding depth reaching 0.5-1m. |
| 28 | Nagbangi I (Amatong) | Flashflood is common. |
| 29 | Nagbangi II | Flashflood common with low turbidity. |
| 30 | Nasuli | Sheet flooding depth reaching 3m high during rainy season. Flashflood very common with high turbidity. Bank scouring/erosion along Sibalom river. Develop an early warning device/system. Constant communication and updates with Brgy. Barangbang on geohazard situation. Identify relocation site for those living along Sibalom River. |
| 31 | Orquia (Igcatumbal) | Flashflood is very common with very high turbidity. |
| 32 | Osorio I | Seasonal flooding with depth of more than 1m. Develop an early warning device/system intended for flood-related hazards. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify relocation site for residents living near Osorio Creek. |
| 33 | Osorio II | Seasonal flooding with depth of more than 1m. Develop an early warning device/system intended for flood-related hazards. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 34 | Panpanan I | Not assessed due to difficulty in accessing the area |
| 35 | Panpanan II | Not assessed due to difficulty in accessing the area |
| 36 | Poblacion | Seasonal flooding with depth of less than 0.5m. Very common occurrence of flashflooding with moderate turbidity. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 37 | Ramon Magsaysay | Flashflood is very common with high turbidity. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 38 | Rizal | Not assessed due to difficulty in accessing the area |
| 39 | San Rafael | Seasonal flooding with depth of more than 1m. Inform residents about the flood related and flashflood hazards. Activate Barangay Disaster Coordinating Council and do contingency planning |
| 40 | Sinundolan | Seasonal flooding with depth of more than 1m. Proposed relocation site: (1) Location- 10◦ 54' 55.2" ; 122◦ 7' 25.7" (2) elevation- 156m (3) Topography- footslopes (4) Geology- sandstone;shale. 3 hectares; 53 houses for relocation. |
| 41 | Sumaray | Not assessed due to difficulty in accessing the area |
| 42 | Trinidad | Seasonal flooding with depth of more than 1m. 100% of the Brgy. Proper affected by flood with 86 houses washed out. Flashflood is very common with moderate turbidity. There should not be any "resettlement" at the current location of Barangay Trinidad. The municipality should request for a geological assessment (e.g., from the Mines and Geosciences Bureau) of the relocation site, once identified. |
| 43 | Tubudan | None |
| 44 | Vilvar | Flashflood very common with moderate turbidity. Sheet flooding depth greater than 1 m. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content) along Sibalom River. |
| 45 | Walker | Not assessed due to difficulty in accessing the area |

XIII. SEBASTE

The result of the MGB Rapid Field Assessment is as follows:

- There are three (3) barangays with high landslide susceptibility (P. Javier, Idio and Alegre).

- There are three (3) barangays with moderate landslide susceptibility (Naujon,

Callan and Bacalan).

- There are four (4) barangays with no landslide susceptibility (Abiera, Poblacion, Aguila and Aras-asan).

Table 1. Results of Landslide Assessment of the Ten (10) Barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | P. Javier | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Barangay P. Javier primary school should be relocated to a safer location due to its proximity to a very steep slope where rockfall is said to have previously occurred. Possible relocation of the whole barangay is recommended due to its dangerous location. |
| 2 | Alegre | Moderate to high (Moderate in barangay proper; high in Sitio Catmon) | Monitor progress of mass movement (e.g. landslide, tension cracks). Observe for presence of mass movement (e.g. landslide, tension cracks). Identify evacuation site. |
| 3 | Idio | Moderate to high; Portions of Puroks 2, 3 and 4 located on/near footslopes are moderately susceptible to landslides | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity. |
| 4 | Naujon | Moderate at the barangay proper, Purok 1 and 3 (footslopes) | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity. |
| 5 | Callan | Moderate at the Barangay Proper, Puroks 1 and 4 | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 6 | Bacalan | Moderate at the barangay proper, Puroks 4 and 5 (footslopes) | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks.) Develop an early warning device/system. |
| 7 | Abiera | None at the barangay proper and moderate at Puroks 1, 2, 6 and 7 | Monitor progress of mass movement (e.g. landslides, tension cracks) in Purok 2. Observe for presence of mass movement (e.g. landslides, tension cracks) 1, 2, 6 and 7. |
| 8 | Poblacion | None at the barangay proper and moderate in Purok 1 and 2 | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 9 | Aguila | None |  |
| 10 | Aras-asan | None |  |

In terms of flood susceptibility ten (10) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the ten (10) Barangays

|  | Barangay | Flood Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Abiera | None | Storm surge affects coastal puroks. |
| 2 | Aguila | Seasonally moderate | Storm surge as well as sheet flooding with depth of 0.5 to 1 meter affects most parts of the barangay. Develop an early warning device/system. Identify evacuation site. Relocate five households living along Banban river as they are susceptible to flash flooding. |
| 3 | Alegre | Seasonally low | Flashflood with moderate turbidity is common. Seasonal flooding with depth of less than 0.5 meter. |
| 4 | Aras-asan | Seasonally moderate | Flashflood with moderate turbidity is common. Bacalan River floods farmlands. Storm surge also affects adjacent low-lying areas. The barangay proper is affected by flood with depth of 0.5 to 1 meter. |
| 5 | Bacalan | Seasonally low | Storm surge and coastal flooding affects Puroks 1, 2 and 5. The barangay proper has low flood susceptibility with dept of less than 0.5 meter. |
| 6 | Callan | Seasonally low at the Barangay Proper and Purok 5; Seasonally moderate in Purok 3 | Coastal areas are susceptible to storm surge. Low flood susceptibility at the Barangay Proper and Purok 5; Seasonally moderate in Purok 3 |
| 7 | Idio | Seasonally low | Coastal and river flooding as well as erosion affect the barangay. Seasonal flooding with depth of less than 0.5 meter. |
| 8 | Naujon | Seasonally high | Coastal portions of the barangay are affected by storm surge. Riverbank erosion along Siya-Siya creek is also noted. The barangay proper is susceptible to flood with depth of greater than 1 meter. |
| 9 | P. Javier | None | Flashflood with moderate turbidity is rare. |
| 10 | Poblacion | Seasonally high | Storm surge affects coastal puroks. The barangay proper has high flood susceptibility with depth of greater than 1 meter. |

XIV.  SIBALOM

The result of the field assessment is as follows:

- There are eleven (11) barangays with high landslide susceptibility (Bongbongan II, Igpanolong, Imparayan, Inabasan, Tulatula, Villafont, Bulalacao, Calo-oy, Lambayagan, Luna, Tordesillas)

- There are sixteen (16) barangays with moderate landslide susceptibility (Igcococ, Igdalaquit, Igparas, Igsuming, Indag-an, Initan, Insarayan, Millamena, Tigbalua I, Tig-ohot, Cadoldolan, Luyang, Tabong-tabong, Valentin Grasparil (Bad-as), Maasin, Tigbalua II)

- There are six (6) barangays with low landslide susceptibility (Bontol, Bugnay, Esperanza III, Salvacion, San Juan, Nagdayao, )

- There are forty (40) barangay centers with no landslide susceptibility.

Table 1. Results of landslide assessment of the seventy-three (73) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Bongbongan II | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device. Identify relocation site for the school and health center. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Sido on geohazard situation. Presence of active landslide near Sibalom river bank and soil creeping at the barangay hall were noted. |
| 2 | Igpanolong | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Relocate Igpanolong Elementary School, Barangay Hall & some houses located at the foot of the very steeply sloping Mount Igpanolong. Activate Barangay Disaster Coordinating Council (BDCC). |
| 3 | Imparayan | High | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslide, tension cracks). Develop an early warning device.Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Villafont. |
| 4 | Inabasan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Sitio Tinubuan, Brgy. Calog. |
| 5 | Tulatula | High | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at brgy. extension. Activate Barangay Disaster Coordinating Council. |
| 6 | Villafont | High | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces.Constant communication and updates with Barangay Salvacion on geohazard situation. |
| 7 | Bulalacao | High especially in in Sitio Bangkal | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system on landslide hazard. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Sitio Bangkal. Constant communication and updates with the Barangay Tula-tula on geohazard situation. Activate BDCC. |
| 8 | Calo-oy | High in Purok 1 | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system on landslide hazard. Observe for saturated ground or seeps in areas that are not typically wet.Observe for sunken or displaced road surfaces.Constant communication and updates with the Barangay Tula-tula on geohazard situation.Activate BDCC. |
| 9 | Luyang | Moderate to high | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device. Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site living at the barangay proper. Relocate barangay hall. Activate the Barangay Disaster Coodinating Council. |
| 10 | Tabong-tabong | Moderate to high | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning system for landslide and flashflood.Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site living at Luna. Constant communication and updates with Brgy. Bontol. Activate the Barangay Disaster Coodinating Council. |
| 11 | Valentin Grasparil (Bad-as) | Moderate to high | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device.Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Purok Labaon. Activate Barangay Disaster Coordinating Council. |
| 12 | Lambayagan | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). Recent escarpments were also noted in the area. |
| 13 | Luna | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify relocation site for the barangay hall. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Iglanot on geohazard situation. Presence of tension cracks in Borotborot. |
| 14 | Tordesillas | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks).Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Sitio Igtangway is bounded by slopes that have high susceptibility to landslide. Observe presence of mass movement. The barangay hall is bounded by slope that is too steep. Slope stability measures must be implemented. |
| 15 | Bontol | Moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 16 | Bugnay | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning system for Landslide.Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces.Constant communication and updates with the Barangay Bontol. Activate Barangay Disaster Coordinating Council. |
| 17 | Esperanza III | Moderate | Observe for presence of mass movement |
| 18 | Salvacion | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Activate the Barangay Disaster Coordinating Council (BDCC). |
| 19 | San Juan | Moderate | Observe for presence of mass movement (e.g., landslides, tension cracks) |
| 20 | Nagdayao | Moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 21 | Maasin | Moderate | Monitor progress of mass movement mass movement (landslide, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 22 | Tigbalua II | Moderate |  |
| 23 | Igcococ | Moderate (proper) to high (Purok 2) | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device.Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site living at Purok 2. Constant communication and updates with Brgy. Tula-tok. Activate the Barangay Disaster Coodinating Council. |
| 24 | Igdalaquit | Moderate at the brgy. Proper; high at Sitio Takas | Monitor progress of mass movement mass movement (landslide, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 25 | Igparas | Moderate for the barangay proper; High for the mountains bounding the eastern side of the barangay. | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Avoid settlement at the foot of the slope of a mountain bounding the eastern/SE part of the barangay as it has high susceptibility to landslide and is fault bounded. Area can be a site of active gully development as it is underlain by easily erodible materials (highly sheared/fractured rocks). |
| 26 | Igsuming | Low to moderate | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for sunken or displaced road surfaces. |
| 27 | Indag-an | Low to moderate at the barangay proper; High at Sitio Nagdayao and Sitio Tarug | Monitor progress and observe for presence of mass movement (e.g. landslides, tension cracks) at sitios Tarug and Nagdayao. Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 28 | Initan | Low | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system for flood and flash flood hazards. Identify evacuation site. Activate BDCC. |
| 29 | Insarayan | Low | Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for staurated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 30 | Millamena | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). Active landslide is also present in the area. |
| 31 | Tigbalua I | Low | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device.Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity; Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Villafont. Tension cracks in the form of terracets along the road going to barangay proper. |
| 32 | Tig-Ohot | Low | Observe for presence of mass movement (e.g. landslides, tension cracks) |
| 33 | Cadoldolan | Low | Observe for presence of mass movement (e.g., landslides, tension cracks) |
| 34 | Egaña | Barangay proper - none; Sitio Limao-high; Sitio Durog-high; Sitio Balabag-high; Sitio Tinhug-high; Sitio Cabarat-high | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks) in Sitios Limao, Durog, Tinhug and Cabarat. Observe for presence of mass movement (e.g. landslides, tension cracks) in other portions of the barangay. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Evidences of mass movement such as tension cracks, active landslides and soil creeping are present in Sitios Limaw, Durog, Balabag, Tinhug and Cabarat. Four (4) households in Sitio Balabag and thirty (30) households in Sitio Tinhub will be affected in case of a major landslide event. |
| 35 | Alangan | None |  |
| 36 | Bari | None |  |
| 37 | Biga-a | None |  |
| 38 | Bongbongan I | None |  |
| 39 | Bongsod | None |  |
| 40 | Cabariuan | None |  |
| 41 | Catmon | None |  |
| 42 | Catungan I | None |  |
| 43 | Catungan II | None |  |
| 44 | Catungan III | None |  |
| 45 | Catungan IV | None |  |
| 46 | Cubay-Napultan | None |  |
| 47 | Cubay-Sermon | None |  |
| 48 | District I (Pob.) | None |  |
| 49 | District II (Pob.) | None |  |
| 50 | District III (Pob.) | None |  |
| 51 | District IV (Pob.) | None |  |
| 52 | Esperanza I | None |  |
| 53 | Esperanza II | None |  |
| 54 | Igdagmay | None | Landslide areas are away from the community. |
| 55 | Iglanot | None |  |
| 56 | Ilabas | None |  |
| 57 | Lacaron | None |  |
| 58 | Lagdo | None |  |
| 59 | Mabini | None |  |
| 60 | Mojon | None |  |
| 61 | Nazareth | None |  |
| 62 | Odiong | None |  |
| 63 | Olaga | None |  |
| 64 | Pampang | None |  |
| 65 | Panlagangan | None |  |
| 66 | Pantao | None |  |
| 67 | Pasong | None |  |
| 68 | Pis-Anan | None |  |
| 69 | Rombang | None |  |
| 70 | Sido | None |  |
| 71 | Solong | None |  |
| 72 | Villahermosa | None |  |
| 73 | Villar | None |  |
| 74 | Cabanbanan | Not assessed due to difficulty in accessing the area |
| 75 | Cabladan | Not assessed due to difficulty in accessing the area |
| 76 | Calog | Not assessed due to difficulty in accessing the area |

In terms of flood assessment, there are seventy-three (73) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the seventy-three (73) barangays

|  | Barangay | Remarks/Recommendations |
| --- | --- | --- |
|  | 1 Alangan | Seasonally flooded with depth 0-0.5 meter. Flash flood with moderate turbidity is rare. |
|  | 2 Bari | Seasonally flooded with depth 0-0.5 meter.Flash flood with low turbidity is rare. |
|  | 3 Biga-a | Seasonally flooded with depth greater than 1 meter. |
|  | 4 Bongbongan I | Seasonally flooded with depth 0.5-1 meter.Sitio Buga is highly susceptible to flood due to overflowing of Bogbongan creek during typhoon season. |
|  | 5 Bongbongan II | Rare occurrence of flood with depth of more than 1 meter. Flash flood with high turbidity is rare. |
|  | 6 Bongsod | None |
|  | 7 Bontol | Seasonally flooded with depth greater than 1 meter. Flashflood is common in Tipuluwan River. Sitio Durog is seasonnally flooded with depth of greater than 1 meter |
|  | 8 Bugnay | Seasonally flooded with depth 0.5-1 meter. River scouring along Maw-it River affects the area.Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
|  | 9 Bulalacao | Riverbank erosion is common in the area. |
|  | 10 Cabanbanan | Not assessed due to difficulty in accessing the area |
|  | 11 Cabariuan | None |
|  | 12 Cabladan | Not assessed due to difficulty in accessing the area |
|  | 13 Cadoldolan | None |
|  | 14 Calog | Not assessed due to difficulty in accessing the area |
|  | 15 Calo-oy | None |
|  | 16 Catmon | None |
|  | 17 Catungan I | Seasonally flooded with depth 0-0.5 meter. Develop an early warning device/system on flood hazard. Identify evacuation site. Puroks 1 and 3 are moderately susceptible to flood affecting 35 and 40 households respectively. The road along barangay proper is seasonally flooded with depth 0 to 0.5 meter. |
|  | 18 Catungan II | Develop an early warning device/system for flood hazard. Identify evacuation site. Purok 1 has low flood susceptibility affecting 5 households. Purok 4 is highly susceptible to flood with depth of greater than 1 meter affecting 5 households. |
|  | 19 Catungan III | Seasonally flooded with depth greater than 1 meter. Purok 6,7 and Sitio Tunga are moderately susceptible to flood with depth 0.5 to 1 meter. |
|  | 20 Catungan IV | Seasonally flooded with depth 0.5-1 meter. Develop an early warning device/system for flood hazard.The barangay proper (Purok 1), Puroks 2 and 3 are moderately susceptible to flood while Puroks 4,5,6 and 7 are highly susceptible to flood. River bank erosion along Sibalom river also affects the area. |
|  | 21 Cubay-Napultan | Seasonally flooded with depth 0-0.5 meter. |
|  | 22 Cubay-Sermon | Flashflood with moderate turbidity is rare. |
|  | 23 District I (Pob.) | Seasonally flooded with depth 0.5-1 meter. Flashflood with moderate turbidity is rare. The barangay is very near Sibalom river. Dredging of the river is recommended since it is heavily silted. |
|  | 24 District II (Pob.) | Seasonally flooded with depth greater than 1 meter. Flooding is caused mainly by insufficient drainage. Construction of dike along Sibalom river is necessary. |
|  | 25 District III (Pob.) | Seasonally flooded with depth 0.5-1 meter.Flashflood with moderate turbidity is rare. Clogging of drainage causes flooding in the area. Construction of dike and declogging of drainage are recommended. |
|  | 26 District IV (Pob.) | Seasonally flooded with depth 0-0.5 meter. Construction of dike along Sibalom and Tipuluan rivers is recommended. |
|  | 27 Egaña | Flooding with depth of greater than 1 meter is mainly due to the overflowing of Tinhub river which affects 5 households at Sitio Limao. About 30 households are situated near Tinhub river which are affected by greater than 1 meter flood. Sitio Cabarat is moderately susceptible to flood affecting 10 households. Flash flooding is very common at Sitios Durog, Tinhub and Cabarat. |
|  | 28 Esperanza I | Seasonally flooded with depth greater than 1 meter. Flash flood with high turbidity is common. |
|  | 29 Esperanza II | Seasonally flooded with depth 0-0.5 meter. |
|  | 30 Esperanza III | Seasonally flooded with depth 0.5-1 meter. |
|  | 31 Igcococ | None |
|  | 32 Igdagmay | Flooding occurs along river banks with less than 1 meter high. |
|  | 33 Igdalaquit | Rare occurrence of flood with depth greater than 1 meter in Sitio Dalipe. Occurrence of flood with depth 0.5-1 meter at Puroks 1 and 2. Flooding occurs only during continous heavy rain. Flash flood with moderate turbidity is rare. |
|  | 34 Iglanot | Rare occurrence of flood with depth 0-0.5 meter. Only ricefields are affected by flooding in the area. Riverbank scouring occurs along Tipuluan river. In Purok 5, around 10 houses were affected by typhoon Frank. Bank scouring at Tipuluan River. |
|  | 35 Igpanolong | Seasonally flooded with depth greater than 1 meter. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Flashflood with moderate turbidity affects the area. |
|  | 36 Igparas | Riverbank erosion could be a problem. Avoid constructing houses immediately adjacent to the bank of the river. |
|  | 37 Igsuming | None |
|  | 38 Ilabas | Seasonally flooded with depth 0-0.5 meter. Overflowing of Sibalom River floods approx. 50 hectares of farmlands during rainy season. |
|  | 39 Imparayan | None |
|  | 40 Inabasan | Bank erosion along the Sibalom and Inabasan rivers is a serious problem. Avoid settlement adjacent to these rivers |
|  | 41 Indag-an | Identify relocation site for residents living at Sitio Tan-agan (riverbank erosion). Flashflood is very common. |
|  | 42 Initan | None |
|  | 43 Insarayan | Seasonally flooded with depth 0-0.5 meter. |
|  | 44 Lacaron | None |
|  | 45 Lagdo | None |
|  | 46 Lambayagan | The barangay also experience riverbank erosion. Flashflood is very common. |
|  | 47 Luna | The barangay also experience riverbank erosion. Flashflood is common. |
|  | 48 Luyang | Flashflood very common |
|  | 49 Maasin | Seasonally flooded with depth greater than 1 meter. Overflowing of San Juan Creek affects ricefields. |
|  | 50 Mabini | None |
|  | 51 Millamena | None |
|  | 52 Mojon | None |
|  | 53 Nagdayao | Seasonally flooded with depth 0-0.5 meter. Floodwaters mainly come from the overflowing of Tipuluan River. |
|  | 54 Nazareth | Seasonally flooded with depth 0-0.5 meter. |
|  | 55 Odiong | Seasonally flooded with depth greater than 1 meter. Floodwaters mainly come from the Odiong Creek; bank erosion along Odiong Creek is a problem. |
|  | 56 Olaga | Seasonally flooded with depth greater than 1 meter. |
|  | 57 Pampang | Seasonally flooded with depth greater than 1 meter. |
|  | 58 Panlagangan | None |
|  | 59 Pantao | Seasonally flooded with depth greater than 1 meter. |
|  | 60 Pasong | None |
|  | 61 Pis-Anan | Flashflood occurs but rare |
|  | 62 Rombang | Seasonally flooded with depth greater than 1 meter. |
|  | 63 Salvacion | Flood rarely occurs and at moderate depth |
|  | 64 San Juan | Seasonally flooded with depth greater than 1 meter. Develop an early warning device.Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living along riverbanks as bank erosion is a problem. Constant communication and updates with Brgy. Sido on the geohazard situatio. |
|  | 65 Sido | Seasonally flooded with depth 0-0.5 meter. Flashflood very common in the area. Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device.Identify evacuation site. Observe for rapid increase/decrease in river water levels, possibly accompanied by increased turbidity. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living near the banks of Sibalom. Constant communication and updates with Brgy. San Juan on the geohazard situation. |
|  | 66 Solong | Seasonally flooded with depth 0.5-1 meter. Flashflood very common in the area. |
|  | 67 Tabong-tabong | None; but flashflood common (residents though are not affected) |
|  | 68 Tigbalua I | None |
|  | 69 Tigbalua II | None at the barangay proper; high at Purok 5; high in areas adjacent to the Nagdayao Creek at Sitio Nagdayao. Riverbank erosion is a problem along Sapa Ike at So. Tarug. |
|  | 70 Tig-Ohot | None |
|  | 71 Tordesillas | Flashflood very common |
|  | 72 Tulatula | Flashflood common |
|  | 73 Valentin Grasparil (Bad-as) | None |
|  | 74 Villafont | None |
|  | 75 Villahermosa | Rare occurrence of flood with depth 0-0.5 meter. |
|  | 76 Villar | Seasonally flooded with depth 0.5-1 meter. |

XV. TIBIAO

The result of the field assessment is as follows:

- There are three (3) barangays with high landslide susceptibility (Castillo, Salazar and Tuno)

- There are two (2) barangays with moderate landslide susceptibility (Alegre and Pitac)

- There are five (5) barangays with low landslide susceptibility (Esparagoza,  Tigbaboy, Importante, La Paz and Santa Ana)

- There are eleven (11) barangay centers with no landslide susceptibility.

Table 1. Results of landslide assessment of the twenty-one (21) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Castillo | High | Series of tension cracks or terracets are very common on slopes surrounding the area. Barangay proper lies on an active slump area/ collapsed surface (sinkhole). Discuss possibility of relocation. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. |
| 2 | Salazar | High | Series of landslides occured along the barangay road making the major route of Brgys. Castillo and Salazar impassable. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Relocate school facilities and rooms away from footslope. Contingency planning on landslide is needed. |
| 3 | Tuno | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Observe for saturated ground or seeps in areas that are not typically wet. |
| 4 | Alegre | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 5 | Pitac | Moderate in barangay proper and high in Sitios Nagayong, Tinangis and Lirag. | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. |
| 6 | Esparagoza | Low (Brgy. Proper); High (on steep slopes) | Barangay is a possible landslide accumulation zone. Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). |
| 7 | Tigbaboy | Low in barangay proper and moderate in Sitio Butong. | Monitor progress of and observe for presence of mass movement (landslide, tension cracks). |
| 8 | Importante | Low in barangay proper and moderate in Sitio Paris. | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. |
| 9 | La Paz | Low | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 10 | Santa Ana | Low | Observe for presence of mass movements; (e.g. landslides, tension cracks). |
| 11 | Amar | None |  |
| 12 | Bandoja | None |  |
| 13 | Malabor | None |  |
| 14 | Martinez | None |  |
| 15 | Natividad | None |  |
| 16 | Poblacion | None |  |
| 17 | San Francisco Norte | None |  |
| 18 | San Francisco Sur | None |  |
| 19 | San Isidro | None |  |
| 20 | Santa Justa | None |  |
| 21 | Santo Rosario | None |  |

In terms of flood assessment, there are sixteen (16) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the twenty-one (21) barangays

|  | Barangay | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Alegre | None |
| 2 | Amar | Seasonal flooding with depth of less than 1m. |
| 3 | Bandoja | Seasonal flooding with depth of less than 1m. Sitio Ulo Kalog experiences perennial flashflood during heavy rains. |
| 4 | Castillo | Flashflooding is very common with high turbidity |
| 5 | Esparagoza | Seasonal flooding with depth of more than 1m. Flashflood occurrence is very common with high turbidity. Barangay is a flashflood exit point. Discuss possibility of relocation. |
| 6 | Importante | Flashflood with moderate turbidity is very common. Avoid settlements along Tibiao river. Seasonal flooding with depth of more than 1m. |
| 7 | La Paz | River erosion at Sitio Lambungauan. |
| 8 | Malabor | Sheet flooding confined in rice fields especially during intense and sustained rainfall. Seasonal flooding with depth of less than 0.5m. |
| 9 | Martinez | Seasonal flooding with depth of more than 1m. |
| 10 | Natividad | Sheet flooding confined in rice fields especially during intense and sustained rainfall. Seasonal flooding with depth of less than 0.5m. |
| 11 | Pitac | None |
| 12 | Poblacion | Seasonal flooding with depth of less than 1m. Relocate 20 households living along Tibiao river. |
| 13 | Salazar | Flashflood with high turbidity is very common along Mamara River. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Contingency planning on flashflood. |
| 14 | San Francisco Norte | None |
| 15 | San Francisco Sur | Seasonal flooding with depth of more than 1m. Flood water from an unnamed creek in Sta. Justa flows toward Purok 1. |
| 16 | San Isidro | None |
| 17 | Santa Ana | Seasonal flooding with depth of more than 1m. Flashflood with moderate turbidity is common. |
| 18 | Santa Justa | Seasonal flooding with depth of more than 1m. Flooding due to overflowing of Tibiao river (also due to clogged drainage). Avoid settlement along riverbanks. Relocate (if possible) eleven families living adjacent Tibiao river. |
| 19 | Santo Rosario | Seasonal flooding with depth of more than 1m. Flashflood with moderate commodity is common. |
| 20 | Tigbaboy | Seasonal flooding with depth of more than 1m. Flashflood with moderate turbidity is very common. Avoid settlement along the banks of Tibiao river. Relocate 11 houses near riverbanks as they may be hit by flashflood. Look for a possible relocation site for Tigbaboy elementary school since it is very near Tibiao river. |
| 21 | Tuno | Avoid settlement along Tibiao river. Relocate 20 households living along Tibiao river. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

XVI.  TOBIAS FORNIER

The result of the field assessment is as follows:

- There are ten (10) barangays with high landslide susceptibility (Abaca, Bariri, Igbalogo, Igcalawagan, Igcapuyas, Nagsubuan, Opsan, Quezon, Samalague and Tacbuyan)

- There are eleven (11) barangays with moderate landslide susceptibility (Nasuli-A, Gamad, Lawigan, Atiotes, Camandagan, Lindero, Igdurarog, Manaling, Portilio, Tene and Igcado)

- There are sixteen (16) barangays with low landslide susceptibility ( Balloscas, Barasanan A, Barasanan B, Igbangcal-B, Igcabuad, Igbangcal-A, Igbangcal-C, Igtugas, Igcadac, Aras-Asan, Arobo, Barasanan C, Danawan, Igcasicad, Igdanlog and  Sto. Tomas)

- There are thirteen (13) barangay centers with no landslide susceptibility.

Table 1. Results of landslide assessment of the fifty (50) barangays

|  | Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Abaca | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Observe saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced roads surfaces. High landslide susceptibility at Concepcion L. Cazeñas Memorial School. Implement slope stabilization measures to protect the school buildings adjacent the steep, unstable slope. Relocate school to a more stable and safer location. |
| 2 | Bariri | High | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 3 | Igbalogo | High | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Igcalawagan on geohazard situation. Activate BDCC. Landslide in Sitio Iraya is 20 meters high, only farmlands are affected. |
| 4 | Igcalawagan | High | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at affected areas in brgy. proper. Constant communication and updates with Brgy. Barasanan on geohazard situation. Activate BDCC. |
| 5 | Igcapuyas | High | Recent landslides, mudflow and widespread creeping were observed.Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content) along Barasanan River. Inform residents of mudflow threats. |
| 6 | Nagsubuan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces.Constant communication and updates with Brgy. Igcalawagan on geohazard situation. Activate BDCC. Sitio Langhangan and Sitio Igcapakul are landslide areas, only farmlands are affected. |
| 7 | Opsan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system for landslide-related hazard. Identify evacuation site. |
| 8 | Quezon | High | Monitor progress of mass movement (e.g. landslide, tension cracks). Observe presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide-related hazard. Observe for saturated ground or seeps in areas that are not typically wet. Identify relocation site for residents living at Brgy. Quezon (water seepage, tension cracks, recent landslides observed in the area) . Activate Barangay Disaster Coordinating Council (BDCC) for disaster preparedness. |
| 9 | Samalague | High | Monitor progress and observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Nasuli-A on geohazard situation. Inform residents on the geohazard situation in the area. |
| 10 | Tacbuyan | High | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Identify evacuation site. Develop an early warning device/system. |
| 11 | Nasuli-A | Moderate - Brgy. Proper; High - on footslopes/steep slopes | Creeping and mudflow can affect the community. A school building was affected by a landslide in 2001. Monitor progress and observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 12 | Gamad | Moderate (brgy. Proper); High (Sitio Atok) | Observe for presence of mass movement (e.g. landslides, tension cracks).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces .Relocate household affected by landslide during the recent typhoon Frank. |
| 13 | Lawigan | Moderate at the barangay proper; High for mountain bounding the northwestern portion of the barangay proper | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Avoid settlement at the foot of steep slopes as slope materials are highly erodible. |
| 14 | Atiotes | Moderate to high | Monitor presence of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 15 | Camandagan | Moderate to high | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks).Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Slopes bounding Ibuk River highly susceptible to landslide and/or bank erosion. This could cause flashflooding in the area. |
| 16 | Lindero | Moderate to high | Monitor presence of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system for landslide-related hazard. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at Brgy. Lindero (some houses are located at the foot of slopes assessed as highly susceptible to landslide). Activate Barangay Disaster Coordinating Council (BDCC). |
| 17 | Igdurarog | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). |
| 18 | Manaling | Moderate | Monitor presence of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Activate Barangay Disaster Coordinating Council (BDCC). |
| 19 | Portilio | Moderate | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). |
| 20 | Tene | Moderate | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 21 | Igcado | Moderate | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Observe for saturated ground seeps in areas that are not typically wet. Inform residents of Purok 5 of potential landslide. |
| 22 | Balloscas | Low (brgy. Proper); High (Sitio Bunga) | Monitor progress of mass movement. Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 23 | Barasanan A | Low (brgy. Proper); High (Sitio Igtaratid & Sitio Igbanwit) | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 24 | Barasanan B | Low (brgy. Proper); High (Sitio Langhaan & Sitio Igkaratid) | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 25 | Igbangcal-B | Low (brgy. Proper); moderate (along road between brgy. Abaca & brgy. Igbangcal-B) | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. |
| 26 | Igcabuad | Low (Brgy. Proper); Moderate(Purok 2) | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 27 | Igbangcal-A | Low to Moderate | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Slope bounding the northern portion of the brgy.'s basketball court is creeping. |
| 28 | Igbangcal-C | Low to moderate | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 29 | Igtugas | Low to Moderate | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Bank erosion also a problem. |
| 30 | Igcadac | Low to moderate (Sitio Igtuba near watershed) | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks).Observe for saturated ground or seeps in areas that are not typically wet.Observe for sunken or displaced road surfaces. |
| 31 | Aras-Asan | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 32 | Arobo | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 33 | Barasanan C | Low | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 34 | Danawan | Low | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 35 | Igcasicad | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 36 | Igdanlog | Low | Observe for presence of mass movement (e.g. landslides, tension cracks). |
| 37 | Sto. Tomas | Low | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). Avoid settlement near landslide areas. |
| 38 | Pacencia | None – Brgy. Proper; High – Sitio Bamban | Monitor progress and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify relocation site for residents living at Sitio Bamban. |
| 39 | Ysulat | None (brgy. Proper); Low (Sitio Panaan) | Monitor progress of mass movement. Observe for presence of mass movement (landslide, tension cracks). |
| 40 | Atabay | None |  |
| 41 | Bagumbayan | None |  |
| 42 | Balud | None |  |
| 43 | Cato-ogan | None |  |
| 44 | Diclum | None |  |
| 45 | Fatima | None |  |
| 46 | Igdalaguit | None |  |
| 47 | Masayo | None |  |
| 48 | Poblacion Norte | None |  |
| 49 | Poblacion Sur | None |  |
| 50 | Villaflor | None |  |

In terms of flood assessment, there are twenty-five (25) barangays found to have flood susceptibility. The results of the assessment are as follows:

Table 2. Results of flood assessment of the fifty (50) barangays

|  | Barangay | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Abaca | Sheet flooding reaches 0.5-1m depth during rainy season. |
| 2 | Aras-Asan | None |
| 3 | Arobo | None |
| 4 | Atabay | None |
| 5 | Atiotes | Flashflood with moderate turbidity affects the area. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Sheet flooding with depth of more than 1m |
| 6 | Bagumbayan | Purok 4 located near creek. Sheet flooding with depth of less than 1m |
| 7 | Balloscas | None |
| 8 | Balud | Sheet flooding reaches less than 0.5m depth during rainy season. |
| 9 | Barasanan A | None |
| 10 | Barasanan B | None |
| 11 | Barasanan C | None |
| 12 | Bariri | None |
| 13 | Camandagan | Active sedimentation within the Ibuk River could result to shallowing of the river. Consider relocating houses near the Ibuk River. Sheet flooding reaches more than 1m depth during rainy season. |
| 14 | Cato-ogan | None |
| 15 | Danawan | None |
| 16 | Diclum | None |
| 17 | Fatima | None |
| 18 | Gamad | None |
| 19 | Igbalogo | Flashflood with moderate turbidity is common. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify an early warning device/system. Sheet flooding reaches more than 1m depth during rainy season. |
| 20 | Igbangcal-A | Sheet flooding reaches less than 0.5m depth during rainy season. |
| 21 | Igbangcal-B | Sheet flooding reaches less than 0.5m depth during rainy season. |
| 22 | Igbangcal-C | Sheet flooding reaches less than 0.5m depth during rainy season. |
| 23 | Igcabuad | None |
| 24 | Igcadac | None |
| 25 | Igcado | Flashflood occurrence is common along along Cabaludan Creek with low turbidity. |
| 26 | Igcalawagan | Flashflood with moderate turbidity is common. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify an early warning device/system. Sheet flooding reaches more than 1m depth |
| 27 | Igcapuyas | Typhoon Frank caused more than 1m flood water but the typhoon that occurred in 2001 had caused a flood depth greater than 1.5m-2m. |
| 28 | Igcasicad | None |
| 29 | Igdalaguit | None |
| 30 | Igdanlog | None |
| 31 | Igdurarog | Seasonal flooding with depth of more than 1m. Common flashflood occurrence with low to moderate turbidity along Igduradog and Barasanan Rivers. Avoid build-up along 2 major rivers. |
| 32 | Igtugas | Flash flood with high turbidity is common. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Sheet flooding with depth of more than 1m during rainy season |
| 33 | Lawigan | Bank erosion also a problem. Avoid settlement immediately adjacent to the river. |
| 34 | Lindero | None |
| 35 | Manaling | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Flashflood with moderate turbidity affects the area. |
| 36 | Masayo | None |
| 37 | Nagsubuan | Flashflood with moderate turbidity is common. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Identify early device/warning system. Seasonal flooding with depth of more than 1m. |
| 38 | Nasuli-A | Flashflood with moderate to high turbidity is very common. Nasuli River is very prone to damming. Inform residents of Puroks on geohazards susceptibility in their area. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content) along Nasuli River. |
| 39 | Opsan | Flood depth is 0-0.5m.Only the ricefields are affected. |
| 40 | Pacencia | Seasonal flooding with depth of less than 1m. |
| 41 | Poblacion Norte | None |
| 42 | Poblacion Sur | Flood depth is 0-0.5m.Only ricefields are affected. |
| 43 | Portilio | None |
| 44 | Quezon | None |
| 45 | Samalague | Rare occurrence of flashflood with moderate turbidity. |
| 46 | Sto. Tomas | Flash flood regularity commonly occurs. Low flash flood turbidity.Flood depth 0-0.5m. |
| 47 | Tacbuyan | Flashflood with high turbidity is common. |
| 48 | Tene | None |
| 49 | Villaflor | None |
| 50 | Ysulat | River scouring along Panaan River. Flood depth 0.5-1m during rainy season. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

XVIII. CALUYA

The result of the MGB Rapid Field Assessment is as follows:

- There are thirteen (13) barangays with high landslide susceptibility (Binanogan,

Bugnay, Bulwangan I, Bulwangan II, Cananghan, Canipayan, Cansilayan, Iglinab, Igmasandig, Pandanan, Takas, Tigmamale and Ubos).

- There are two (2) barangays with moderate landslide susceptibility (Lublub and

San Agustin).

- There are three (3) barangays with low landslide susceptibility (Boroc-Boroc, Bunsod and Manlacbo).

- There are four (4) barangays that were not assessed due to difficulty in accessing the area (Alon, Bakiang, Busog and Culyat).

Table 1. Results of Landslide Assessment of the Eighteen (18) Barangays

| Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Binanogan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents at Sitio Igcabugao. Constant communication and updates with Barangay Iglinab & Takas on geohazard situation. Relocation site/housing project to be assessed by MGB-DENR-Region 6 (Iloilo City) for its suitability is highly recommended. Coordinate with Mayor's office regarding this. Four houses transferred to housing project (Brgy. Proper). |
| 2 | Bugnay | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Tigmamale on geohazard situation. Activate BDCC. Relocate houses located at landslide areas. Sitio Buri, Bunga, Hinugisan and Tawo are landslide areas. One person died during the landslide in Sitio Buri. |

XVII. VALDERAMA

The result of the MGB Rapid Field Assessment is as follows:

- There are thirteen (13) barangays with high landslide susceptibility (Binanogan,

Bugnay, Bulwangan I, Bulwangan II, Cananghan, Canipayan, Cansilayan, Iglinab, Igmasandig, Pandanan, Takas, Tigmamale and Ubos).

- There are two (2) barangays with moderate landslide susceptibility (Lublub and

San Agustin).

- There are three (3) barangays with low landslide susceptibility (Boroc-Boroc, Bunsod and Manlacbo).

- There are four (4) barangays that were not assessed due to difficulty in accessing the area (Alon, Bakiang, Busog and Culyat).

Table 1. Results of Landslide Assessment of the Eighteen (18) Barangays

| Barangay | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Binanogan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents at Sitio Igcabugao. Constant communication and updates with Barangay Iglinab & Takas on geohazard situation. Relocation site/housing project to be assessed by MGB-DENR-Region 6 (Iloilo City) for its suitability is highly recommended. Coordinate with Mayor's office regarding this. Four houses transferred to housing project (Brgy. Proper). |
| 2 | Bugnay | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Tigmamale on geohazard situation. Activate BDCC. Relocate houses located at landslide areas. Sitio Buri, Bunga, Hinugisan and Tawo are landslide areas. One person died during the landslide in Sitio Buri. |
| 3 | Bulwangan I | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Poblacion on geohazard situation. Landslides occur at Sitio Badiangan and Igkitkit Mountain. Road subsidence at Sitio Huna. |
| 4 | Bulwangan II | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Bulwangan I on geohazard situation. No houses should be constructed at the landslide area. Debris slide occurs at Lam-an Mountain. |
| 5 | Cananghan | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Identify relocation site for the brgy. hall. Constant communication and updates with Brgy. Cansilayan and Pandanan on geohazard situation. |
| 6 | Canipayan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Bulwangan I on geohazard situation. Landslide occurs at Sitio Igcapla. |
| 7 | Cansilayan | High | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Identify relocation site for the school. Constant communication and updates with Brgy. Culyat on geohazard situation. |
| 8 | Iglinab | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Pandanan on geohazard situation. Avoid construction of houses at the landslide area. Landslide occurs at Sitios Igang and Pajo. |
| 9 | Igmasandig | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Municipality of Valderama on geohazard situation. Activate BDCC. |
| 10 | Pandanan | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Cananghan on geohazard situation. Landslide occurs at Lobo, Lanas, Sitio Balunos and Takas where the Army Camp is located. |
| 11 | Takas | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Landslide occurs at Sitios Igtilad and Tangke. |
| 12 | Tigmamale | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy. Bugnay on geohazard situation. |
| 13 | Ubos | High | Monitor progress of mass movement and observe for presence of mass movement (landslide, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content).Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Takas on geohazard situation. Landslides observed at the mountains belonging to the barangay. |
| 14 | Lublub | Moderate | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. |
| 15 | San Agustin | Moderate | Monitor progress of mass movement (landslides, tension cracks). Observe for presence of mass movement (landslides, tension cracks). Develop an early warning device/system. Observe for sunken or displaced road surfaces. Constant communication and updates with Brgy.Lublub on geohazard situation. |
| 16 | Boroc-Boroc | Low | Monitor progress of mass movement (landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Sitio Lapayan and Tigbrising are possible landslide areas. |
| 17 | Bunsod | Low | Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with the Barangay Boroc-Boroc on geohazard situation. Activate BDCC. Landslides in Sitio Uma affected farmlands. |
| 18 | Manlacbo | Low | Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communication and updates with Barangay Bunsod on geohazard situation. Activate BDCC. |

In terms of flood susceptibility, eighteen (18) barangays experience varying degrees of flooding. The results are as follows:

Table 2. Results of Flood Assessment of the Eighteen (18) Barangays

| Barangay | Remarks/ Recommendations |
| --- | --- |
| 1 | Binanogan | Flashflood with very high turbidity is rare. Sheet flooding depth greater than 1 m. |
| 2 | Boroc-Boroc | The barangay is highly susceptible to flood with depth of greater than 1 meter. Previous barangay proper should be evacuated as it is being eroded by the Cangaranan River. Residents must transfer to the relocation site assessed by MGB-6. Constant communication and updates with Barangay Manlacbo and Pandanan. Activate BDCC. Relocation site already identified and assessed by the municipal government and MGB-Region 6. Develop an early warning device/system. |
| 3 | Bugnay | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning system. The barangay proper rarely experiences flooding (low flood susceptibility). |
| 4 | Bulwangan I | Flashflood with moderate turbidity is rare. Sheet flooding depth is greater than 1 m. Bank scouring/erosion along Cangaranan River also a problem. |
| 5 | Bulwangan II | Flashflood with moderate turbidity is rare. Sheet flooding depth is greater than 1 m. |
| 6 | Bunsod | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning system. Flooding with depth of more than 1 meter occurs in the area during typhoon season. |
| 7 | Cananghan | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). The barangay proper rarely experiences flooding (low flood susceptibility). |
| 8 | Canipayan | Flashflood with moderate turbidity is rare. Sheet flooding depth is greater than 1 m. Bank scouring/erosion along Cangaranan River. Also a problem Three houses located near a landslide area. The barangay hall is located at the meander of Cangaranan River and will be in danger of being washed away by the river. |
| 9 | Cansilayan | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). The barangay rarely experiences flooding (low flood susceptibility). |
| 10 | Iglinab | Flashflood with very high turbidity is rare. Sheet flooding depth is greater than 1 m. Bank scouring/erosion also a problem. |
| 11 | Igmasandig | Flashflood with high turbidity is very common. Sheet flooding depth is greater than 1 m. Develop an early warning system. |
| 12 | Lublub | Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). The barangay rarely experiences flooding (low flood susceptibility). |
| 13 | Manlacbo | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). The barangay rarely experiences flooding (low flood susceptibility). |
| 14 | Pandanan | Flashflood with moderate turbidity is rare. Sheet flooding depth is greater than 1 m. Bank scouring/erosion also a problem. |
| 15 | San Agustin | Flashflood with moderate turbidity affects the area. |
| 16 | Takas | Flashflood with very high turbidity is rare. Sheet flooding depth is greater than 1 m. Bank scouring/erosion also a problem. |
| 17 | Tigmamale | Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Develop an early warning system. The barangay is seasonally flooded with depth of greater than 1 meter. |
| 18 | Ubos | Flashflood with moderate turbidity is common. Sheet flooding depth is greater than 1 m. |

XVIII. CALUYA

Table 1. Results of Landslide Assessment of the Eighteen (18) Barangays

|  | Barangay Name | Landslide Susceptibility Rating |
| --- | --- | --- |
| 1 | Alegria | Moderate |
| 2 | Bacong | Moderate |
| 3 | Banago | Low. Recommendations: Monitor progress of mass movement (e.g. landslides, tension cracks). |
| 4 | Bonbon | None |
| 5 | Dawis | Low. Recommendations: Observe presence of mass movement (e,g, landslides, tension cracks). |
| 6 | Dionela | Low |
| 7 | Harigue | None |
| 8 | Hininga-an | Low. Recommendations: Observe presence of mass movement (e,g, landslides, tension cracks). |
| 9 | Imba | None |
| 10 | Masanag | None |
| 11 | Poblacion | None |
| 12 | Sabang | Low. Recommendations: Observe presence of mass movement (e,g, landslides, tension cracks). |
| 13 | Salamento | Low. Recommendations: Observe presence of mass movement (e,g, landslides, tension cracks). |
| 14 | Semirara | Low |
| 15 | Sibato | None |
| 16 | Sibay | None |
| 17 | Sibolo | None |
| 18 | Tinogboc | Low |

Table 2. Results of Flood Assessment of the Eighteen (18) Barangays

| Barangay Name | Remarks/Recommendations |
| --- | --- |
| Alegria | Coastal flooding. Sheet flooding with moderate depth occurs seasonally. |
| Bacong | Coastal Flooding. Sheet flooding of moderate depth. |
| Banago | Coastal Flooding. Sheet flooding with depth of >1.0m occurs seasonally. Recommendations: Develop an early warning device/system. Identify evacuation site. Constant communication and updates with Brgy. Imba on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| Bonbon | Coastal flooding, storm surge. Sheet flooding with moderate depth occurs seasonally. |
| Dawis | Coastal flooding, 1 meter high tide, storm. Recommendations: Develop an early warning device/system. Identify evacuation site. Constant communication and updates with Brgy. Sabang/ Hininga-an on geohazard situation. Activate Barangay |
| Dionela | Coastal flooding. Sheet flooding with moderate depth occurs seasonally. |
| Harigue | Coastal flooding. Sheet flooding with 0.0-0.5m depth. |
| Hininga-an | Sheet flooding with 0.0-0.5m depth occurs seasonally. Recommendations: Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and updates with Brgy. Dawis on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| Imba | Coastal flooding. Sheet flooding with 0.0-0.5m depth occurs seasonally. Recommedations: Develop an early warning device/system (coastal flooding/storm surge). Constant communication and updates with Brgy. Banago on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| Masanag | Coastal flooding. Sheet flooding with moderate depth occurs seasonally. Recommedations: Develop an early warning device/system (coastal flooding/storm surge). Constant communication and updates with Brgy. Banago on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| Poblacion | Coastal flooding, storm surge. Sheet flooding with moderate depth occurs seasonally. Recommedations: Develop an early warning device/system (coastal flooding/storm surge). Constant communication and updates with Brgy. Banago on geohazard situation. |
| Sabang | Coastal flooding. Sheet flooding with 0.0-0.5m depth occurs seasonally. Recommendations: Develop an early warning device/system (storm surge/coastal flooding). Activate Barangay Disaster Coordinating Council. |
| Salamento | Sheet flooding with depth of 0.0-0.5m occurs seasonally (during rainy season). Develop an early warning device/system (flooding). Observe for rapid increase/decrease in creek/river water levels, possibly accompanied by increased turbidity (soil content). Constant communication and updates with Brgy. Hininga-an on geohazard situation. Activate Barangay Disaster Coordinating Council (BDCC). |
| Semirara | Coastal flooding. |
| Sibay | Coastal flooding. |
| Sibato | None. |
| Sibolo | None. |
| Tinogboc | Coastal flooding. |