RESULTS OF THE MGB GEOHAZARD ASSESSMENT

OF BARANGAYS IN BUENAVISTA, GUIMARAS

In line with the recent Presidential Directive and NDCC resolutions following the February 17 Southern Leyte landslide incident, and the need to fast track the geohazard mapping program of the Philippines, two (2) geologists from the Mines and Geosciences Bureau 6 (MGB), namely: Mae Y. Magarzo and Leilanie O. Suerte conducted a field assessment of 36 barangays in Buenavista, Guimaras on June 2010. The field assessment focused on both the landslide and flood susceptibilities of the barangays.

In terms of landslide susceptibility, each barangay was rated low, moderate or high. The rating parameters are as follows:

High

- Presence of active and/ or recent landslides

- Presence of numerous and large tension cracks

- Areas with drainages that are prone to debris damming

- Areas with numerous old landslides/escarpments

- Steep slopes

- Presence of weak/rock slope materials

- Structures (joints, beds) dipping towards the slope face

- Nearness to faults

Moderate

- Areas with indicative and/or old landslides

- Presence of small tension cracks

- Moderate slopes

Low

- Low to gently sloping

- No evidence of mass movement

The rating of each barangay, unless specified, refers to the barangay proper.

The barangays were presented with a Landslide Threat Advisory, when appropriate. The Advisory informs the barangays of their susceptibility to landslides and contains the corresponding recommendations particular to the barangay.

In terms of flood susceptibility, the barangays were defined in terms of the depth and frequency of flooding.

The result of the MGB Rapid Field Assessment is as follows:

- Brgy. Magsaysay, Montpiller, Sawang and Zaldivar are highly susceptible to landslide.

- Brgy.  Agsanayan, Avila, Banban, Cansilayan, Getulio, Mabini, Old Poblacion, Rizal, San Pedro, Tacay, Taminla, Tanag, Tinadtaran are moderately susceptible to landslide.

- Brgy. Bacjao, Dagsaan, Daragan, Salvacion, San Pedro, San Nicolas, San Isidro and Umilig have low susceptibility to landslide.

- Brgy. East Valencia, San Roque, Sto. Rosario and Tastasan are not susceptible to landslide but some barangays have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

- Brgy. Mclain, Navalas, Nazaret, New Poblacion, Piña, San Miguel and Supang are not susceptible to landslide.

Table1. Results of Landslide Assessment of the barangays

|  | Barangay Name | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Magsaysay | High | Purok Bangkiling and Cabungahan are mountainous areas. The school served as the evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide/flood-related hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Zaldivar/Sto. Rosario on geohazard situation. Houses must not be constructed at the footslopes of the mountains. |
| 2 | Montpiller | High | Sitio Minuro, Nabuyao, Mura and Palhi are mountainous areas. Rock type consists of limestone beds dipping towards the road. Evacuation site consists of church and school. Uses megaphone as an early warning device for disasters. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Rizal/ Caragan on geohazard situation. Houses must not be constructed at the footslopes of the mountains. |
| 3 | Sawang | High | Portions of Purok 3 and 2 are mountainous. There are areas in Purok 2 with impending rock slides which could affect 5 houses. In Purok 1, 3 houses will be affected by rock slides. Evacuation site is the day care center. Uses cellphone as early warning device for disasters. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Zaldivar/ Dagsa-an on geohazard situation. Relocate houses at the foot of the mountains. Houses must not be constructed at the foot of the mountains. |
| 4 | Zaldivar | High | Presence of landslide in Purok 1-Proper. The barangay hall, day care center and health center served as evacuation centers. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Sawang/ Magsaysay/ Salvacion on geohazard situation. |
| 5 | Agsanayan | Moderate | The barangay experiences bank scouring. Uses cellphones as early warning device. Schools are used as evacuation site. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. San Isidro/ Piña/ Tinadtaran/ San Roque on geohazard situation. |
| 6 | Avila | Moderate in Barangay Proper Sitio Canatbo and Sitio Carasan are also moderately susceptible to landslides | RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. |
| 7 | Banban | Moderate | RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. |
| 8 | Cansilayan | Moderate | RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. |
| 9 | Getulio | Moderate | RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. |
| 10 | Mabini | Moderate in Barangay Proper High in some sitios and puroks. | Uses cellphone as early warning device. The barangay hall and school served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide/flood-related hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Zaldivar/Sto. Rosario on geohazard situation. Houses must not be constructed at the banks of the river and footslopes of the mountains. |
| 11 | Old Poblacion | Moderate in Barangay Proper High in the Catholic Cemetery (Purok 1) | Barangay hall, school and church are used as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Sto. Rosario/ San Isidro/ Rizal on geohazard situation. |
| 12 | Rizal | Moderate in Barangay Proper High in Purok Yacht and Frigate | Old/inactive landslides (2005) in Purok Galleon. Uses bells as early warning device. Barangay hall, school and church are used as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Sto. Rosario/ Montpiller/ Daragan on geohazard situation. |
| 13 | San Pedro | Moderate | RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. |
| 14 | Tacay | Moderate in Barangay Proper High in Sitio Tubod and Bungol | Rock slide occurs once in a while in the barangay. Uses cellphone as early warning device. Barangay hall, school, day care center, auditorium served as evacuation sites. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Taminla/ San Pedro/ Getulio on geohazard situation. Houses must not be constructed at the footslopes and slopes of the mountains, near banks of rivers and creeks. Residents near rivers/creeks must be on alert and ready to evacuate during floods. |
| 15 | Taminla | Moderate High in Sitio Lusod | Uses cellphone as early warning device. The school served as evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied By increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Tacay/ Mabini/ Dagsa-an on geohazard situation. |
| 16 | Tanag | Moderate | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. |
| 17 | Tinadtaran | Moderate | Barangay hall and church are used as evacuation sites. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. San Lorenzo/ Gaban/ East Valencia/ Agsanayan on geohazard situation. |
| 18 | Bacjao | Low | RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system. Identify evacuation site. Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Activate baranagay disaster coordinating council. |
| 19 | Dagsa-an | Low High in footslopes of hills/mountains with houses/ schools (e.g. Buro-Buro) | Some footslopes of hills/mountains with houses are highly susceptible to landslides/rockfall. Uses cellphone as early warning device. The school served as evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents of 5 houses in Sitio Buro-Buro downslope of loose rocks. Constant communications and updates with Brgy. Sawang/ Taminla/ Zaldivar on geohazard situation. Houses must not be constructed at the footslopes/slopes of mountains. |
| 20 | Daragan | Low High in Purok Masagana and Mabuhay | Uses cellphone as early warning device. The school and barangay hall served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Montpiller/ Piña/ Rizal on geohazard situation. |
| 21 | Salvacion | Low | Uses cellphone as early warning device. The barangay hall and school served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Sto. Rosario/ New and Old Pob./ Dagsa-an on geohazard situation. |
| 22 | San Fernando | Low | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. |
| 23 | San Nicolas | Low | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. |
| 24 | San Isidro | Low | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. San Roque/ Agsanayan/ Old Poblacion on geohazard situation. |
| 25 | Umilig | Low | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. |
| 26 | East Valencia | None in Barangay Proper Moderate in Sitio Cagay | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. |
| 27 | Mclain | None |  |
| 28 | Navalas | None |  |
| 29 | Nazaret | None |  |
| 30 | New Poblacion | None |  |
| 31 | Piña | None |  |
| 32 | San Miguel | None |  |
| 33 | San Roque | None in Barangay Proper Moderate in Purok 4 | Uses foot patrol as early warning system. The school and barangay hall served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Tastasan/ Tinadtaran/ Agsanayan on geohazard situation. |
| 34 | Sto. Rosario | None in Barangay Proper High in Purok Pantalan, Mabinuligon, Mapainubuson | In 2009, 2 houses were affected by rockslide. About 100 houses are landslide prone in Purok Pantalan, Mabinuligon and Mapainubuson. Uses cellphone as early warning device. The barangay hall served as the evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site for residents living at footslopes of mountains. Constant communications and updates with Brgy. Old Poblacion/ Salvacion/ Rizal/ Magsaysay on geohazard situation. Houses must not be constructed at the footslopes of mountains. Residents living in landslide prone areas must be alert and ready to evacuate during heavy rain and strong typhoons. |
| 35 | Supang | None |  |
| 36 | Tastasan | None in Barangay Proper Low in Purok III | RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. |

In terms of flood susceptibility, the 36 barangays experience varying degrees of flooding. The results are as follows:

Table 2.  Results of Flood Assessment of the Barangays

|  | Barangay Name | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Agsanayan | In Purok Maputli, flashflood with low turbidity occurs commonly and sheet flooding with low depth seasonally occurs. It takes 2-3 hours for flood waters to subside and rice fields are usually affected. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 2 | Avila | Some flooding are observed in the boundary of Avila with Umilig and East Valencia. The barangay is also affected by storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 3 | Banban | The barangay is drained by small creeks and is not affected by flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 4 | Bacjao (Calumingan) | The barangay is affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 5 | Cansilayan | The barangay is drained by small creeks/river and is not affected by flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 6 | Dagsa-an | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. Rice fields are usually affected during flooding. Floodwaters may take 3 days to subside. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 7 | Daragan | Flashflood with low turbidity commonly occurs in Purok Masagana and Mabuhay. Sheet flooding with low depth occurs seasonally in Purok Masagana and Mabuhay. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 8 | East Valencia (Mantangingi) | Sheet flooding with moderate depth occurs seasonally. The high school and the back of the elementary school are flood-prone. The barangay is also prone to coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 9 | Getulio (Ili) | The barangay is drained by small creeks (between Tacay and Getulio) and is not affected by sheet flooding. Coastal flooding and storm surges affect the area. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 10 | Mabini | Presence of depression in Purok Charlie. Flashflood with low turbidity rarely occurs in Purok Charlie. Sheet flooding with low depth also occurs rarely in this area. The barangay proper is not affected by flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 11 | Magsaysay | Flashflood with low turbidity occurs commonly. Sheet flooding with low depth occurs rarely. The barangay is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Houses must not be constructed at the banks of the river. |
| 12 | Mclain | Sheet flooding with moderate depth occurs seasonally. Flooding is due to drainage problem and low-lying topography. Floodwaters subside after 30 minutes. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 13 | Montpiller | Flashflood with low turbidity commonly occurs. Sheet flooding with low depth occurs seasonally. Purok Minuro has inadequate drainage system. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Houses must not be constructed at the banks of rivers and creeks. |
| 14 | Navalas | The barangay is affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. Houses must be constructed away from the coastline, banks of rivers/creeks. |
| 15 | Nazaret | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. |
| 16 | New Poblacion (Calingao) | Flooding is observed in Purok VI due to its low-lying topography. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Construct an efficient drainage system. |
| 17 | Old Poblacion (Daan Banwa) | Flashflood with low turbidity and sheet flood with high depth rarely occurs in the barangay proper, Purok 4, 5, 6 and Daliran. The barangay proper is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 18 | Piña | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. |
| 19 | Rizal | Flashflood with low turbidity and sheet flood with high depth rarely occurs in the barangay proper and Purok Galleon. A fishpond was destroyed in 2004 due to heavy rains. The barangay proper is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 20 | Salvacion (Ambolong) | Flashflood with low turbidity and sheet flooding with high depth occurs rarely in the boundary of the barangay proper and Purok Malipayon. Presence of depression in Purok Diaya. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 21 | San Fernando | Flooding is confined along creeks, which isolates residents/ students from the barangay. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 22 | San Isidro | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. |
| 23 | San Miguel | The barangay is prone to coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 24 | San Nicolas (Tabao) | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. |
| 25 | San Pedro (Bating) | The barangay proper is drained by small creeks, hence it is not affected by flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 26 | San Roque | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. |
| 27 | Sto. Rosario | Flashflood with low turbidity and sheet flooding with low depth occurs rarely in the barangay proper. In Purok Mabinuligon, flashflood with low turbidity occurs commonly and sheet flooding with low depth occurs seasonally. The barangay is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 28 | Sawang | Affected by storm surges and coastal flooding. Not affected by sheet flooding. |
| 29 | Supang | Sheet flooding with low depth occurs seasonally. In Purok Gumamela, and Dancing Lady, floodwaters may reached up to 1 foot. Flooding is due to low-lying topography of the barangay. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 30 | Tacay | Flashflood with low turbidity commonly occurs. Flooding with moderate depth occurs seasonally. Affected by storm surge and coastal flooding. Sitio Bungol also experiences very common and low turbidity flashfloods, flooding with low depth seasonally. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Houses must not be constructed near the banks of rivers/creeks. Residents living along rivers/creeks must be alert and ready to evacuate in case of flooding events. |
| 31 | Taminla | Flashflood with low turbidity and flooding with high depth occurs rarely (only during heavy rains and typhoons). RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 32 | Tanag | Ricefields are mostly flooded during heavy rain. Coastal flooding and storm surges affect the barangay. Coastal erosion is observed in Lusong. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 33 | Tastasan | Flooding is observed in Purok II and III due to low-lying topography of the area. About 30 households are affected by flooding in this area. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 34 | Tinadtaran | Flashflood with low turbidity and sheet flooding with high depth occurs rarely in Purok Nueva Villa, Manaul Proper, Simbaran Creek. Ricefields are flooded during strong rains and typhoons. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 35 | Umilig | Sheet flooding with high depth occurs seasonally. Problem with drainage system. During flooding events, rice fields and roads are affected. The barangay is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Construction/rehabilitation of drainage system. |
| 36 | Zaldivar | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. The barangay is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

## Geohazard Assessment Team

| Mae Y. Magarzo Supervising Science Research Specialist OIC, Geosciences Division MGB – Region VI | Leilanie O. Suerte, D. Eng. Senior Science Research Specialist MGB – Region VI |
| --- | --- |

RESULTS OF THE MGB GEOHAZARD ASSESSMENT

OF BARANGAYS IN JORDAN, GUIMARAS

In line with the recent Presidential Directive and NDCC resolutions following the February 17 Southern Leyte landslide incident, and the need to fast track the geohazard mapping program of the Philippines, Mae Y. Magarzo, a geologist from the Mines and Geosciences Bureau 6 (MGB) conducted a field assessment of 14 barangays in Jordan, Guimaras on June 2010. The field assessment focused on both the landslide and flood susceptibilities of the barangays.

In terms of landslide susceptibility, each barangay was rated low, moderate or high. The rating parameters are as follows:

High

- Presence of active and/ or recent landslides

- Presence of numerous and large tension cracks

- Areas with drainages that are prone to debris damming

- Areas with numerous old landslides/escarpments

- Steep slopes

- Presence of weak/rock slope materials

- Structures (joints, beds) dipping towards the slope face

- Nearness to faults

Moderate

- Areas with indicative and/or old landslides

- Presence of small tension cracks

- Moderate slopes

Low

- Low to gently sloping

- No evidence of mass movement

The rating of each barangay, unless specified, refers to the barangay proper.

The barangays were presented with a Landslide Threat Advisory, when appropriate. The Advisory informs the barangays of their susceptibility to landslides and contains the corresponding recommendations particular to the barangay.

In terms of flood susceptibility, the barangays were defined in terms of the depth and frequency of flooding.

The result of the MGB Rapid Field Assessment is as follows:

- Brgy. Buluangan, Espinosa and Morobuan are highly susceptible to landslide.

- Brgy. Bugnay, San Miguel, Sta. Teresa and Sinapsapan are moderately susceptible to landslide.

- Brgy. Alaguisoc, Balcon Maravilla and Balcon Melliza have low susceptibility to landslide but some barangays have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

- Brgy. Hoskyn, Lawi, Poblacion and Rizal are not susceptible to landslide but some barangays have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

Table1. Results of Landslide Assessment of the barangays

|  | Barangay Name | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Buluangan | High | The area near the boundary of Buluangan (Jordan) and Ravina (Sibunag) are highly prone to landslides. Sitio Tukod/ Curipaw/ Nogkasan/ Pob;acion I are located in high areas. Bank scouring is also noted. Uses radio and school bell as early warning devices. The school served as the evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Lawi/ Ravina/ Sta. Teresa on geohazard situation. |
| 2 | Espinosa | High in Barangay Proper and all sitios | Rock slides are common in the barangay. There are houses located at footslopes of the mountains. Uses handset as early warning device. The school served as the evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Sinapsapan/ Sta. Teresa on geohazard situation. Houses must not be constructed at the footslopes of the mountains. |
| 3 | Morobuan | High | The barangay hall served as the evacuation site. Uses handset as an early warning device for disasters. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Balcon Maravilla/ Espinosa on geohazard situation. |
| 4 | Bugnay | Moderate | Soil creep occurs along the national road in Sitio Bugna and Ilawod during rainy season. In Sitio Tanod, one (1) foot horizontal displacement and 5 meters long tension cracks are noted. Uses cellphone as early warning device. The barangay hall, school and chapel served as the evacuation site. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Constancia/ San Miguel/ Alaguisoc on geohazard situation. |
| 5 | San Miguel | Moderate | Evacuation site is the Central School. Uses handset/megaphone as early warning device for disasters. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Bugnay/ Sta. Teresa/ Alaguisoc on geohazard situation. |
| 6 | Sta. Teresa | Moderate | Sitio Carp and Cahil are located in high areas. Evacuation site is the school. Uses megaphone as early warning device for disasters. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. San Miguel on geohazard situation. |
| 7 | Sinapsapan | Moderate in Barangay Proper High in Sitio Tarawis | Presence of rock slide in Sitio Tarawis. The health center served as evacuation center. Uses megaphone/handset as early warning device. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Sta. Teresa/ Lawi/ Espinosa on geohazard situation. |
| 8 | Alaguisoc | Low in Barangay proper Moderate in some areas. | The barangay experiences bank scouring. Uses handset as early warning device. Schools are used as evacuation site. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. San Miguel/ Balcon Melliza/ Bugnay on geohazard situation. |
| 9 | Balcon Maravilla | Low in Barangay Proper High in portions of Sitio Timbad and Capituguan | Uses handset as early warning device. The school serves as evacuation site. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Balcon Melliza/ Morobuan geohazard situation. |
| 10 | Balcon Melliza | Low in Barangay Proper High in Sitio Singcalang | Rock slide occurs in Sitio Singcalang. Uses handset as early warning device. The school served as the evacuation site. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Balcon Maravilla/ Hoskyn/ Poblacion/ Alaguisoc on geohazard situation. |
| 11 | Hoskyn | None in Barangay Proper High in Sitio Baluarte, Sambag, Cabadiangan, Lagbas, Tabuc Suba | Rock slide is observed at the back of the school, in Sitio Baluarte, Sambag, Cabadiangan, Lagbas and Tabuc Suba. Displaced road along the coast is noted. Uses handset as early warning device. The health center, day care and school served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movements (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Rizal/ Poblacion/ Balcon Melliza on geohazard situation. Activate barangay disaster coordinating council. |
| 12 | Lawi | None in Barangay Proper High in Sitio Baybay and Matagsim | Rock slide is noted in Sitio Baybay and Matagsim. About more than 30 houses are prone to rock slide in these areas. In Sitio Matagsim, the kitchen of a house was destroyed by a boulder during a rock slide episode. The school and chapel served as evacuation sites. RECOMMENDATIONS: Observe for presence of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Identify relocation site and relocate residents living at the foot slopes of the mountains. Constant communications and updates with Brgy. Sta. Teresa/ Buluangan/ Sinapsapan on geohazard situation. Residents at the foot slopes of the mountains must be on alert and ready to evacuate in case of landslides. Houses must not be constructed at the foot slopes and slopes of mountains. |
| 13 | Poblacion | None in Barangay Proper High in Sitio Dingle. | Landslide was noted in Sitio Dingle. Uses handset as early warning device. The Central School served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Rizal/ Hoskyn on geohazard situation. |
| 14 | Rizal | None in Barangay Proper High in Sitio Lanag and Teodoro | Rock slide is noted in Sitio Lanag and Sitio Teodoro. Uses handset as early warning device. The school served as evacuation sites. RECOMMENDATIONS: Monitor progress of mass movement (e.g. landslides, tension cracks). Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Hoskyn/ Poblacion on geohazard situation. |

In terms of flood susceptibility, the 14 barangays experience varying degrees of flooding. The results are as follows:

Table 2.  Results of Flood Assessment of the Barangays

|  | Barangay Name | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Alaguisoc | No reports of flooding in the barangay. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 2 | Balcon Maravilla | Flashflood with low turbidity and sheet flooding with low depth rarely occurs. Affected areas are mostly farmlands. One cause of flooding is the inadequate drainage system. The barangay is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 3 | Balcon Melliza | Flashflood with low turbidity occurs commonly. Sheet flooding with low to high depth occurs seasonally. Flooded area is from the barangay proper going towards the highway. One cause of flooding is the inadequate drainage system. Coastal areas are affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Construct/rehabilitate drainage system to accommodate water from the river. |
| 4 | Bugnay | Flashflood with low turbidity and sheet flooding with high depth occurs rarely. In Sitio Ilawod, 1 house is located only 60 meters from the riverbank. In Sitio Bugna, 1 house is located 25-30 meters from the riverbank. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 5 | Buluangan | Flashflood with moderate turbidity occurs commonly. Sheet flooding with high depth occurs seasonally. Part of the barangay is near the coast. Back flow of seawater to the creek is also noted. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 6 | Espinosa | Flashflood with low turbidity and sheet flooding with low depth occurs commonly. Sheet flooding with low depth occurs seasonally. Sitio Abuyo, Manguliad and Cabaling are affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 7 | Hoskyn | Flashflood with low turbidity and sheet flooding with low depth rarely occurs. The barangay is also affected by coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 8 | Lawi | Flashflood with low turbidity and sheet flooding with low depth rarely occurs. The barangay is also prone to coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 9 | Morobuan | Flashflood with low turbidity and sheet flooding with low depth occurs rarely in the barangay proper and Sitio Badiang. Coastal flooding and storm surges affect the area. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Identify relocation site and relocate the residents of Proper I (houses located along the Morobuan River). |
| 10 | Poblacion | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. In Sitio Bagatnan and barangay proper, about 15 houses are affected by flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 11 | Rizal | In the barangay proper, flashflood with low turbidity and sheet flooding with low depth occurs rarely. In Sitio Lanag, where a depression is present, flashflood with low turbidity commonly occurs and sheet flooding with low depth seasonally occurs. The barangay is also affected by coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Houses must not be constructed at the banks of the river. |
| 12 | San Miguel | Sheet flooding with moderate depth occurs seasonally. Flooding is due to drainage problem and low-lying topography. Floodwaters subside after 30 minutes. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 13 | Sta. Teresa | Flashflood with low turbidity and sheet flooding with low depth rarely occurs Flooding in the area is caused by strong, heavy and prolonged rainfall. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Construct/rehabilitate drainage system. |
| 14 | Sinapsapan | Flashflood with low turbidity and sheet flooding with low depth rarely occurs in the barangay proper and Sitio Catmon. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

## Geohazard Assessment Team

| Mae Y. Magarzo Supervising Science Research Specialist OIC, Geosciences Division MGB – Region VI |  |
| --- | --- |

RESULTS OF THE MGB GEOHAZARD ASSESSMENT

OF BARANGAYS IN NUEVA VALENCIA, GUIMARAS

In line with the recent Presidential Directive and NDCC resolutions following the February 17 Southern Leyte landslide incident, and the need to fast track the geohazard mapping program of the Philippines, two (2) geologists from the Mines and Geosciences Bureau 6 (MGB), namely: Mae Y. Magarzo and Leilanie O. Suerte conducted a field assessment of 22 barangays in Nueva Valencia, Guimaras on June 2010. The field assessment focused on both the landslide and flood susceptibilities of the barangays.

In terms of landslide susceptibility, each barangay was rated low, moderate or high. The rating parameters are as follows:

High

- Presence of active and/ or recent landslides

- Presence of numerous and large tension cracks

- Areas with drainages that are prone to debris damming

- Areas with numerous old landslides/escarpments

- Steep slopes

- Presence of weak/rock slope materials

- Structures (joints, beds) dipping towards the slope face

- Nearness to faults

Moderate

- Areas with indicative and/or old landslides

- Presence of small tension cracks

- Moderate slopes

Low

- Low to gently sloping

- No evidence of mass movement

The rating of each barangay, unless specified, refers to the barangay proper.

The barangays were presented with a Landslide Threat Advisory, when appropriate. The Advisory informs the barangays of their susceptibility to landslides and contains the corresponding recommendations particular to the barangay.

In terms of flood susceptibility, the barangays were defined in terms of the depth and frequency of flooding.

The result of the MGB Rapid Field Assessment is as follows:

- Brgy. La Paz and Magamay are highly susceptible to landslide.

- Brgy. Cabalagnan, Guiwanon, Pandaraonon, Panobolon and San Roque have low susceptibility to landslide but some barangays have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

- Brgy. Calaya, Canhawan, Concordia Sur, Dolores, Igang, Igdarapdap, Lanipe, Lucmayan, Napandong, Oracon Sur, Poblacion, Salvacion, San Antonio, Sto. Domingo and Tando are not susceptible to landslide but some barangays have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

Table1. Results of Landslide Assessment of the barangays

|  | Barangay Name | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | La Paz | High | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide/flood-related hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. San Roque on geohazard situation. Inform residents living at the footslopes and slopes of mountains/ hills of possible occurrences of mass movement. |
| 2 | Magamay | High | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide/flood-related hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Pandaraonan on geohazard situation. Inform residents living at the footslopes and slopes of mountains/ hills of possible occurrences of mass movement. |
| 3 | Cabalagnan | Low High in Sitio Baybay | Four (4) houses will be affected by possible mass movement in Sitio Baybay. RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for landslide/flood-related hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompaniedby increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. La Paz/ Pandaraonan on geohazard situation. Inform residents living at the footslopes and slopes of mountains/ hills of possible occurrences of mass movement. |
| 4 | Guiwanon | Low | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for presence of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Panobolon/ Cabalagnan on geohazard situation. |
| 5 | Pandaraonan | Low | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Magamay on geohazard situation. Inform residents living at the footslopes and slopes of mountains/ hills of possible occurrences of mass movement. |
| 6 | Panobolon | Low | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Guiwanon and Cabalagnan on geohazard situation. Activate barangay disaster coordinating council. |
| 7 | San Roque | Low | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Lucmayan/ Salvacion on geohazard situation. Activate barangay disaster coordinating council. Inform residents living at the footslopes and slopes of mountains/ hills and those living along San Roque River of possible occurrences of mass movement and flooding events, respectively. |
| 8 | Calaya | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 9 | Canhawan | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 10 | Concordia Sur | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 11 | Dolores | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 12 | Igang | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 13 | Igdarapdap | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 14 | Lanipe | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 15 | Lucmayan | None in Barangay Proper High in Sitio Dungraan | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for rapid increase/ decrease in creek/river water levels possibly accompanied by increased turbidity (soil content). Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with Brgy. Lucmayan/ Salvacion on geohazard situation. Activate barangay disaster coordinating council. Inform residents living at the footslopes and slopes of mountains/ hills of possible occurrences of mass movement. |
| 16 | Napandong | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 17 | Oracon Sur | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 18 | Poblacion | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 19 | Salvacion | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 20 | San Antonio | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 21 | Sto. Domingo | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 22 | Tando | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |

In terms of flood susceptibility, the 22 barangays experience varying degrees of flooding. The results are as follows:

Table 2.  Results of Flood Assessment of the Barangays

|  | Barangay Name | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Cabalagnan | No reported flooding in the barangay proper. Coastal areas are prone to coastal flooding and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 2 | Calaya | No reported flooding in the barangay proper. Bank scouring and erosion is observed along Sibunag River. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 3 | Canhawan | Flashflood with high turbidity occurs commonly. Sheet flooding with moderate depth occurs seasonally. The barangay is also prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Inform residents living along Canhawan Creek of possible flashflood. |
| 4 | Concordia Sur | No reported flooding in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 5 | Dolores | No reported flooding in the barangay proper. Flooding is reported in rice fields. Coastal areas are prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 6 | Guiwanon | The island is susceptible to coastal flooding, erosion and storm surges. Coastal erosion (about 5 meters wide and 100 meters long) is reported in the shorelines of the island. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 7 | Igang | Flashflood with low turbidity and sheet flooding with moderate depth occurs rarely. Flooding occurred in Nalundan and Igang River during Typhoon Undang, where floodwaters reached 1 meter and took 1 day to subside. Coastal areas are prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 8 | Igdarapdap | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. Coastal areas are prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Inform residents living along Paco and Canhawan Creek of possible flooding events. |
| 9 | Lanipe | No reported flooding in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 10 | La Paz | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. Sitio Tigkalayo and Almansok are prone to coastal flooding and storm surges. During flooding events, water overflows into the roads. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 11 | Lucmayan | Flooding occurs in Lucmayan River during heavy rain and typhoons. Sitio Dungraan is prone to storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Houses must not be constructed at the banks of the river. |
| 12 | Magamay | Flashflood with low turbidity occurs commonly. Sheet flooding with low depth occurs rarely. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 13 | Napandong | No reported flooding in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Houses must not be constructed at the banks of rivers and creeks. |
| 14 | Oracon Sur | Flashflood with low turbidity and sheet flood with low depth rarely occurs. RECOMMENDATIONS: Observe for rapid increase/decrease in sea water levels. Houses must be constructed away from banks of rivers/creeks. |
| 15 | Pandaraonon | No reported flooding in the barangay proper. In Sitio Abaca, 9 houses are affected by coastal hazards. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 16 | Panobolon | No reported flooding in the barangay proper. The island is prone to sea level rise, coastal flooding, erosion and storm surges. It is reported that the south side of the island is affected by sea level rise. Since the 1970s, about 200 meters of coastline have been submerged due to sea level rise. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 17 | Poblacion | No reported flooding in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 18 | Salvacion | No reported flooding in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |
| 19 | San Antonio | Flashflood with low turbidity and sheet flood with low depth rarely occurs. In Sitio Pandan, 7 houses are affected by flooding of the Sibunag River. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Inform residents along Sibunag River of possible flooding events. |
| 20 | San Roque | Flashflood with moderate turbidity occurs rarely. Sheet flooding with moderate depth occurs seasonally. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 21 | Sto. Domingo | Flashflood with moderate turbidity commonly occurs. Sheet flooding with moderate depth seasonally occurs. Areas near Igang and Magamay River are prone to flashflood and sheet flood. Coastal areas are prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 22 | Tando | Flashflood with low turbidity and sheet flood with low depth rarely occurs. Coastal areas are prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

## Geohazard Assessment Team

| Mae Y. Magarzo Supervising Science Research Specialist OIC, Geosciences Division MGB – Region VI | Leilanie O. Suerte, D. Eng. Senior Science Research Specialist MGB – Region VI |
| --- | --- |

RESULTS OF THE MGB GEOHAZARD ASSESSMENT

OF BARANGAYS IN SAN LORENZO, GUIMARAS

In line with the recent Presidential Directive and NDCC resolutions following the February 17 Southern Leyte landslide incident, and the need to fast track the geohazard mapping program of the Philippines, Leilanie O. Suerte, a geologist from the Mines and Geosciences Bureau 6 (MGB) conducted a field assessment of 12 barangays in San Lorenzo, Guimaras on June 2010. The field assessment focused on both the landslide and flood susceptibilities of the barangays.

In terms of landslide susceptibility, each barangay was rated low, moderate or high. The rating parameters are as follows:

High

- Presence of active and/ or recent landslides

- Presence of numerous and large tension cracks

- Areas with drainages that are prone to debris damming

- Areas with numerous old landslides/escarpments

- Steep slopes

- Presence of weak/rock slope materials

- Structures (joints, beds) dipping towards the slope face

- Nearness to faults

Moderate

- Areas with indicative and/or old landslides

- Presence of small tension cracks

- Moderate slopes

Low

- Low to gently sloping

- No evidence of mass movement

The rating of each barangay, unless specified, refers to the barangay proper.

The barangays were presented with a Landslide Threat Advisory, when appropriate. The Advisory informs the barangays of their susceptibility to landslides and contains the corresponding recommendations particular to the barangay.

In terms of flood susceptibility, the barangays were defined in terms of the depth and frequency of flooding.

The result of the MGB Rapid Field Assessment is as follows:

- Brgy. M. Chavez has low to moderate susceptibility to landslide.

- Brgy. Aguilar, Constancia, Gaban, Sapal and Tamborong have low susceptibility to landslide but most of these baranagys have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

- Brgy.  Cabano, Cabungahan, Igcawayan, San Enrique, Sebario and Suclaran are not susceptible to landslide but some areas in these barangays are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

Table1. Results of Landslide Assessment of the barangays

|  | Barangay Name | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | M. Chavez | Low to Moderate | About 10 houses in Bukid Bugtong are susceptible to landslides. Reported landslides in the barangay during Typhoon Frank. RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes of Bukid Bugtong and along the coast/river during heavy rain and typhoons. |
| 2 | Aguilar | Low in Barangay Proper, Sitio Tacas, Camansi and Ilawod Moderate in Sitio Bantayan and Teprosan | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 3 | Constancia | Low in Barangay Proper Moderate in Bukid Ayakan and Lambibi | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 4 | Gaban | Low in Barangay Proper Moderate in Sitio Bantayan | Reported landslides in the barangay during Typhoon Frank. RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 5 | Sapal | Low in Barangay Proper Moderate in Sitio Libas and Banderahan | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 6 | Tamborong | Low in Barangay Proper Moderate in Sitio Teprosan and Gamut | Headwaters of river systems are prone to landslides and flashfloods. RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 7 | Cabano | None in Barangay Proper Low to Moderate in Sitio Nabuyong, Tangaw, Banaba and Turo-Turo Mountains | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 8 | Cabungahan | None in Barangay Proper Low to Moderate in Sitio Takas and Buyuan | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 9 | Igcawayan | None in Barangay Proper Low to Moderate in Sitio Banderahan | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 10 | San Enrique | None in Barangay Proper Moderate in Sitio Mantasig and Matagsing | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 11 | Sebario | None in Barangay Proper Low to Moderate in Sitio Ilaya and Ipil | About 100 houses have low to moderate susceptibility to mass movements in Sitio Ilaya and Ipil. RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |
| 12 | Suclaran | None in Barangay Proper Low in Sitio Takas | RECOMMENDATIONS: Observe for presence and monitor progress of mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation. Activate barangay disaster coordinating council. Evacuate residents at the footslopes and slopes of mountains/ hills during heavy rain and typhoons. |

In terms of flood susceptibility, the 12 barangays experience varying degrees of flooding. The results are as follows:

Table 2.  Results of Flood Assessment of the Barangays

|  | Barangay Name | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Aguilar | Flood-prone (flashflood or sheet flood) areas include Sitio Camansi, Tacas, Teprosan, Bantayan and along the Cabano River. Some portions of the roads are impassable when the Cabano River overflows. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Construct footbridge in areas where the Cabano River overflows. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 2 | Cabano | Flashflood with moderate turbidity commonly occurs in the Poblacion and Sitio Tumanda. Sheet flooding with high depth occurs seasonally. Sitio Igcabano and Balabago are affected by coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. Monitor and report coastal erosion to CENRO/DENR. |
| 3 | Cabungahan | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. |
| 4 | Constancia | Flood-prone areas include Sitio Munan, Sitio Kuripao and Sitio Gaway-Gaway. More than 40 houses are located in these areas. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 5 | Gaban | Flooding not reported in the barangay proper. Sitio Pandan is a flood-prone area. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 6 | Igcawayan | Flashflood with low turbidity commonly occurs and sheet flooding with high depth occurs seasonally along Igcawayan River. The barangay is also affected by coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 7 | M. Chavez | Flashflood with low turbidity occurs rarely. Sheet flooding with low depth rarely seasonally. Sitio Miagos, Calle 11 and Sitio Paglamutan is also prone to flooding. The barangay is also affected by coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 8 | San Enrique | Areas near the rivers/creeks and coast are flood-prone areas. The barangay is prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 9 | Sapal | Flooding not reported in the barangay proper. In Sitio Natapan, flooding in the overflow makes the road impassable. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Construct footbridge in areas where the overflow is always flooded. |
| 10 | Sebario | Sitio Riverside is prone to flooding. The barangay is prone to coastal flooding, erosion and storm surges. About 50 houses are prone to flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 11 | Suclaran | Flashflood with moderate turbidity occurs commonly. Sheet flooding with high depth occurs seasonally. Flood-prone areas include Tinuran Creek and Sitio Baybay. The barangay is prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |
| 12 | Tamborong | Flooding is not reported in the barangay proper. Sitio Gamut may be susceptible to flashfloods. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Evacuate residents in flood-prone areas during heavy rain and typhoons. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

## Geohazard Assessment Team

| Leilanie O. Suerte, D. Eng. Senior Science Research Specialist MGB – Region VI MGB – Region VI |  |
| --- | --- |

RESULTS OF THE MGB GEOHAZARD ASSESSMENT

OF BARANGAYS IN SIBUNAG, GUIMARAS

In line with the recent Presidential Directive and NDCC resolutions following the February 17 Southern Leyte landslide incident, and the need to fast track the geohazard mapping program of the Philippines, two (2) geologists from the Mines and Geosciences Bureau 6 (MGB), namely: Mae Y. Magarzo and Leilanie O. Suerte conducted a field assessment of 14 barangays in Sibunag, Guimaras on June 2010. The field assessment focused on both the landslide and flood susceptibilities of the barangays.

In terms of landslide susceptibility, each barangay was rated low, moderate or high. The rating parameters are as follows:

High

- Presence of active and/ or recent landslides

- Presence of numerous and large tension cracks

- Areas with drainages that are prone to debris damming

- Areas with numerous old landslides/escarpments

- Steep slopes

- Presence of weak/rock slope materials

- Structures (joints, beds) dipping towards the slope face

- Nearness to faults

Moderate

- Areas with indicative and/or old landslides

- Presence of small tension cracks

- Moderate slopes

Low

- Low to gently sloping

- No evidence of mass movement

The rating of each barangay, unless specified, refers to the barangay proper.

The barangays were presented with a Landslide Threat Advisory, when appropriate. The Advisory informs the barangays of their susceptibility to landslides and contains the corresponding recommendations particular to the barangay.

In terms of flood susceptibility, the barangays were defined in terms of the depth and frequency of flooding.

The result of the MGB Rapid Field Assessment is as follows:

- All assessed barangays are not susceptible to landslide but Brgy. Dasal have areas that are given higher ratings due to the evidences of mass movement observed on slopes surrounding the area.

- Brgy. Inampulugan, a private island, was not visited by the geohazard assessment team.

Table1. Results of Landslide Assessment of the barangays

|  | Barangay Name | Landslide Susceptibility Rating | Remarks/ Recommendations |
| --- | --- | --- | --- |
| 1 | Alegria | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 2 | Ayangan | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 3 | Bubog | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 4 | Concordia Norte | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. |
| 5 | Dasal | None in Barangay Proper High in Sitio Pitongan. | In Sitio Pitongan, 10 houses are prone to mass movement. RECOMMENDATIONS: Observe for presence of and monitor progress mass movement (e.g. landslides, tension cracks). Develop an early warning device/system intended for hazard prevention. Identify evacuation site. Observe for saturated ground or seeps in areas that are not typically wet. Observe for sunken or displaced road surfaces. Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. Inform residents living at the slopes of mountains for possible occurrences of mass movements. |
| 6 | Inampulugan |  | Private island, not visited by the geohazard team. |
| 7 | Maabay | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 8 | Millan | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 9 | Oracon Norte | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 10 | Ravina | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 11 | Sabang | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 12 | San Isidro | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 13 | Sebaste | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |
| 14 | Tanglad | None | RECOMMENDATIONS: Constant communications and updates with nearby barangays on geohazard situation/ disasters. Activate barangay disaster coordinating council. |

In terms of flood susceptibility, the 14 barangays experience varying degrees of flooding. The results are as follows:

Table 2.  Results of Flood Assessment of the Barangays

|  | Barangay Name | Remarks/ Recommendations |
| --- | --- | --- |
| 1 | Alegria | Flashflood with high turbidity commonly occurs. Sheet flooding with high depth seasonally occurs. About 15 houses near Sibunag River may be affected by flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Inform residents living along Sibunag river of possible flashflood and sheet floods. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 2 | Ayangan | No reported flooding in the barangay proper. Areas near Sibunag River are prone to flooding. Floodwaters may take 7 hours to subside. In Sitio Canag, bank scouring and erosion are reported. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Inform residents living along Sibunag river of possible flashflood and sheet floods. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 3 | Bubog | Flashflood with low turbidity and sheet flooding with low depth rarely occurs. Areas near Bubog Creek are prone to flooding. Floodwaters may take several hours to subside. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Inform residents living along Sibunag river of possible flashflood and sheet floods. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 4 | Concordia Norte | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 5 | Dasal | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. Areas near Bigo River are prone to flooding. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Inform residents living along Bigo River of possible flashflood and sheet floods. |
| 6 | Inampulugan | Private island, not visited by geohazard team. |
| 7 | Maabay | Flashflood with low turbidity and sheet flooding with low depth occurs during heavy rains and typhoons. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 8 | Millan | Flooding during typhoons is confined in rice fields. Floodwaters may take 3-4 days to subside. Bank scouring and erosion are reported in the banks of creeks. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 9 | Oracon Norte | Flooding is confined in rice fields. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Develop early warning device/system for hazard prevention. |
| 10 | Ravina | Flooding is not reported in the barangay proper. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Develop early warning device/system for hazard prevention. |
| 11 | Sabang | Flashflood with low turbidity and sheet flooding with low depth occurs rarely. The coastal area, with 15 houses, is also affected by coastal flooding, erosion and storm surges. The road is affected by and is impassable during high tide. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Houses must not be constructed near the shoreline. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 12 | San Isidro | Flooding is confined in rice fields. The barangay is also affected by coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river water levels. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 13 | Sebaste | Areas near Malbag Creek are prone to flooding. About 20 houses located in coastal areas are prone to coastal flooding, erosion and storm surges. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Develop early warning device/system for hazard prevention. Identify evacuation site. |
| 14 | Tanglad | Flooding is confined in rice fields. RECOMMENDATIONS: Observe for rapid increase/decrease in creek/river/sea water levels. Develop early warning device/system for hazard prevention. |

It should be noted that these susceptibility ratings were arrived at as of this field assessment. However, the rating could advance (e.g., from low to moderate, and moderate to high) as the mass movement progresses. Hence, the MGB constantly recommends strict and continuous monitoring by the barangays.

## Geohazard Assessment Team

| Mae Y. Magarzo Supervising Science Research Specialist OIC, Geosciences Division MGB – Region VI | Leilanie O. Suerte, D. Eng. Senior Science Research Specialist MGB – Region VI |
| --- | --- |